## Slide 1: 776 Computer Vision
Jan-Michael Frahm
Fall 2015

## Slide 2: Capturing light
Source: A. Efros

## Slide 3: Light transport
slide: R. Szeliski

## Slide 4: What is light?
Electromagnetic radiation (EMR) moving along rays in space
  R(l) is EMR, measured in units of power (watts)
    l is wavelength
Light field
  We can describe all of the light in the scene by specifying the radiation (or “radiance” along all light rays) arriving at every point in space and from every direction
slide: R. Szeliski

## Slide 5: Conventional versus light field camera
slide: Marc Levoy

## Slide 6
Conventional versus light field camera
slide: Marc Levoy

## Slide 7: Conventional versus light field camera
slide: Marc Levoy

## Slide 8: Prototype camera
4000 × 4000 pixels ÷ 292 × 292 lenses = 14 × 14 pixels per lens
Contax medium format camera
Kodak 16-megapixel sensor
Adaptive Optics microlens array
125μ square-sided microlenses
slide: Marc Levoy

## Slide 9
slide: Marc Levoy

## Slide 10: Digitally stopping-down
stopping down = summing only the central portion of each microlens
Σ
Σ
f / N light field camera, with P × P pixels under each microlens, can produce views as sharp as an f / (N × P) conventional camera
slide: Marc Levoy

## Slide 11: Digital refocusing
refocusing = summing windows extracted from several microlenses
Σ
Σ
f/N light field camera can produce views with a shallow depth of field ( f / N ) focused anywhere within the depth of field of an f / (N × P) camera
images: Marc Levoy

## Slide 12: Example of digital refocusing
images: Marc Levoy

## Slide 13: Extending the depth of field
conventional photograph, main lens at f / 22
conventional photograph, main lens at f / 4
light field, main lens at f / 4, after all-focus algorithm [Agarwala 2004]
images: Marc Levoy

## Slide 14: Digitally moving the observer
moving the observer = moving the window we extract from the microlenses
Σ
Σ
images: Marc Levoy

## Slide 15: Example of moving the observer
slide: Marc Levoy

## Slide 16: Moving backward and forward
slide: Marc Levoy

## Slide 17: The visible light spectrum
We “see” electromagnetic radiation in a range of wavelengths

## Slide 18: Light spectrum
The appearance of light depends on its power spectrum
  How much power (or energy) at each wavelength
daylight
tungsten bulb
Our visual system converts a light spectrum into “color”
  This is a rather complex transformation
image: R. Szeliski
Human Luminance Sensitivity Function

## Slide 19: Brightness contrast and constancy
The apparent brightness depends on the surrounding region
  brightness contrast: a constant colored region seems lighter or darker depending on the surroundings:
    http://www.sandlotscience.com/Contrast/Checker_Board_2.htm
  brightness constancy: a surface looks the same under widely varying lighting conditions.
slide modified from : R. Szeliski

## Slide 20: Light response is nonlinear
Our visual system has a large dynamic range
  We can resolve both light and dark things at the same time (~20 bit)
  One mechanism for achieving this is that we sense light intensity on a logarithmic scale
    an exponential intensity ramp will be seen as a linear ramp
    retina has about 6.5 bit dynamic range
  Another mechanism is adaptation
    rods and cones adapt to be more sensitive in low light, less sensitive in bright light.
  Eye’s dynamic range is adjusted with every saccade
Notes: retina has 100:1 contrast ratio, adjusted during any saccade => 1, 000, 000 :1 for the eye

## Slide 21: After images
Tired photoreceptors
  Send out negative response after a strong stimulus
http://www.michaelbach.de/ot/mot_adaptSpiral/index.html

## Slide 22: Light transport
slide: R. Szeliski

## Slide 23: Light sources
Basic types
  point source
  directional source
    a point source that is infinitely far away
  area source
    a union of point sources
slide: R. Szeliski

## Slide 24: The interaction of light and matter
What happens when a light ray hits a point on an object?
  Some of the light gets absorbed
    converted to other forms of energy (e.g., heat)
  Some gets transmitted through the object
    possibly bent, through “refraction”
  Some gets reflected
    as we saw before, it could be reflected in multiple directions at once
Let’s consider the case of reflection in detail
  In the most general case, a single incoming ray could be reflected in all directions. How can we describe the amount of light reflected in each direction?
slide: R. Szeliski

## Slide 25: The BRDF
The Bidirectional Reflection Distribution Function
  Given an incoming ray and outgoing ray what proportion of the incoming light is reflected along outgoing ray?
Answer given by the BRDF:
surface normal
slide: R. Szeliski

## Slide 26: BRDFs can be incredibly complicated…
slide: S. Lazebnik

## Slide 27
from Steve Marschner

## Slide 28
from Steve Marschner

## Slide 29: Constraints on the BRDF
Energy conservation
  Quantity of outgoing light ≤ quantity of incident light
    integral of BRDF ≤ 1
Helmholtz reciprocity
  reversing the path of light produces the same reflectance
=
slide: R. Szeliski

## Slide 30: Diffuse reflection
Diffuse reflection
  Dull, matte surfaces like chalk or latex paint
  Microfacets scatter incoming light randomly
  Effect is that light is reflected equally in all directions
slide: R. Szeliski

## Slide 31: Diffuse reflection
Diffuse reflection governed by Lambert’s law
  Viewed brightness does not depend on viewing direction
  Brightness does depend on direction of illumination
  This is the model most often used in computer vision
L, N, V unit vectors
Ie = outgoing radiance
Ii = incoming radiance
Lambert’s Law:
BRDF for Lambertian surface
slide: R. Szeliski

## Slide 32: Lambertian Sphere

## Slide 33
Why does the Full Moon have a flat appearance?
The moon appears matte (or diffuse)
But still, edges of the moon look bright
(not close to zero) when illuminated by
earth’s radiance.
Thanks to Michael Oren, Shree Nayar, Ravi Ramamoorthi, Pat Hanrahan

## Slide 34
Why does the Full Moon have a flat appearance?
Lambertian Spheres and Moon Photos illuminated similarly
Thanks to Michael Oren, Shree Nayar, Ravi Ramamoorthi, Pat Hanrahan

## Slide 35
Surface Roughness Causes Flat Appearance
Actual Vase
Lambertian Vase
Thanks to Michael Oren, Shree Nayar, Ravi Ramamoorthi, Pat Hanrahan

## Slide 36
Surface Roughness Causes Flat Appearance
Increasing surface roughness
Lambertian model
Valid for only SMOOTH MATTE surfaces.
Bad for ROUGH MATTE surfaces.
Thanks to Michael Oren, Shree Nayar, Ravi Ramamoorthi, Pat Hanrahan

## Slide 37: Specular reflection
For a perfect mirror, light is reflected about N
Near-perfect mirrors have a highlight around R
  common model:
slide: R. Szeliski

## Slide 38: Specular reflection
Moving the light source
Changing ns
slide: R. Szeliski

## Slide 39: Blurred Highlights and Surface Roughness - RECAP
Roughness

## Slide 40
Oren-Nayar Model – Main Points
Physically Based Model for Diffuse Reflection.
Based on Geometric Optics.
Explains view dependent appearance in Matte Surfaces
Take into account partial inter reflections.
Roughness represented
Lambertian model is simply an extreme case with
roughness equal to zero.

## Slide 41
View Dependence of Matte Surfaces - Key Observation
Overall brightness increases as the angle between the source and viewing direction decreases. WHY?
Pixels have finite areas. As the viewing direction changes, different mixes between dark and bright are added up to give pixel brightness.

## Slide 42: Phong illumination model
Phong approximation of surface reflectance
  Assume reflectance is modeled by three components
    Diffuse term
    Specular term
    Ambient term (to compensate for inter-reflected light)
L, N, V unit vectors
Ie = outgoing radiance
Ii = incoming radiance
Ia = ambient light
ka = ambient light reflectance factor
(x)+ = max(x, 0)
slide: R. Szeliski

## Slide 43: BRDF models
Phenomenological
  Phong
  Ward
  Lafortune et al.
  Ashikhmin et al.
Physical
  Cook-Torrance
  Dichromatic
  He et al.
Here we’re listing only some well-known examples
slide: R. Szeliski

## Slide 44: Measuring the BRDF
Gonioreflectometer
  Device for capturing the BRDF by moving a camera + light source
  Need careful control of illumination, environment
traditional
design by Greg Ward
slide: R. Szeliski

## Slide 45: Gonioreflectometer
image credit: www.mdpi.com

## Slide 46: BRDF databases
MERL (Matusik et al.): 100 isotropic, 4 nonisotropic, dense
CURET (Columbia-Utrect): 60 samples, more sparsely sampled, but also bidirectional texure functions (BTF)
slide: R. Szeliski

## Slide 47: Image formation
How bright is the image of a scene point?
slide: S. Lazebnik

## Slide 48: Radiometry
Radiometry is the science of light energy measurement
Radiance energy carried by a ray energy/solid angle [watts per steradian per square meter (W·sr−1·m−2)]
image: R. Szeliski
Notes: Radiance characterizes the light emitted by the surface
Irradiance characterizes the light received by an optical device/eye

## Slide 49: Radiometry: Measuring light
The basic setup: a light source is sending radiation to a surface patch
What matters:
  How big the source and the patch “look” to each other
source
patch
slide: S. Lazebnik
Notes: Consider the hemisphere of directions at a given point on the surface. Light can only arrive at the point along these directions. If two different sources result in exactly the same amount of radiation arriving along every incoming direction, they must have the same effect on the surface.

## Slide 50: Solid Angle
The solid angle subtended by a region at a point is the area projected on a unit sphere centered at that point
  Units: steradians
The solid angle dw subtended by a patch of area dA is given by:
slide: S. Lazebnik
A
Notes: dA projected onto surface of the sphere of radius r: dA cos theta
Ratio of surface areas of spheres of radii 1 and r: 4 pi / (4 pi r^2) = 1/r^2

## Slide 51: Radiance
Radiance (L): energy carried by a ray
  Power per unit area perpendicular to the direction of travel, per unit solid angle
  Units: Watts per square meter per steradian (W m-2 sr-1)
dA
n
θ
dω
slide: S. Lazebnik
Notes: P is area orthogonal to the incoming light ray

## Slide 52: Radiometry
Radiometry is the science of light energy measurement
Radiance energy carried by a ray energy/solid angle [watts per steradian per square meter (W·sr−1·m−2)]
Irradiance energy per unit area falling on a surface
image: R. Szeliski
Notes: Radiance characterizes the light emitted by the surface
Irradiance characterizes the light received by an optical device/eye

## Slide 53: Irradiance
dA
Irradiance (E): energy arriving at a surface
  Incident power per unit area not foreshortened
  Units: W m-2
  For a surface receiving radiance L coming in from dw the corresponding irradiance is
n
θ
dω
slide: S. Lazebnik

## Slide 54: Radiometry of thin lenses
L: Radiance emitted from P toward P’
E: Irradiance falling on P’ from the lens
What is the relationship between E and L?
slide: S. Lazebnik

## Slide 55: Radiometry of thin lenses
o
dA
dA’
Area of the lens:
The power δP received by the lens from P is
The irradiance received at P’ is
The radiance emitted from the lens towards P’ is
Solid angle subtended by the lens at P’
slide: S. Lazebnik
Notes: See section 4.2.3 of F&P
Explanation of last equation:
Use the definition of irradiance from slide 7
Compute the solid angle subtended by the lens at P’ using the definition on slide 4

## Slide 56: Radiometry of thin lenses
Image irradiance is linearly related to scene radiance
Irradiance is proportional to the area of the lens and inversely proportional to the squared distance between the lens and the image plane
The irradiance falls off as the angle α between the viewing ray and the optical axis increases
slide: S. Lazebnik
Notes: Explain the difference between the cos^4 alpha effect and vignetting: the former effect has nothing to do with light getting lost in the lens system but is a basic radiometric property even of a perfect lens; vignetting is usually much stronger.

## Slide 57: From light rays to pixel values
Camera response function: the mapping f from irradiance to pixel values
  Useful if we want to estimate material properties
  Enables us to create high dynamic range images
Source: S. Seitz, P. Debevec

## Slide 58: From light rays to pixel values
Camera response function: the mapping f from irradiance to pixel values
Source: S. Seitz, P. Debevec
For more info
  P. E. Debevec and J. Malik. Recovering High Dynamic Range Radiance Maps from Photographs. In SIGGRAPH 97, August 1997

## Slide 59: Photometric stereo (shape from shading)
Can we reconstruct the shape of an object based on shading cues?
Luca della Robbia, Cantoria, 1438