## Slide 1: COMP541 Sequential Circuits
Montek Singh
Sep 17, 2014

## Slide 2: Topics
Sequential Circuits
  Latches
  Flip Flops
Verilog for sequential design
  Example: A simple counter

## Slide 3: Sequential Circuits
State of system is information stored/memorized
  State and inputs determine outputs

## Slide 4: Types of Sequential Circuits
Synchronous
  State changes synchronized by one or more clocks
Asynchronous
  There are no clocks, but changes are triggered by events (e.g., inputs changing)

## Slide 5: Clocking of Synchronous
Changes enabled by clock

## Slide 6: Comparison
Synchronous
  Easier to analyze because can factor out gate delays
  Set clock so changes occur before next clock pulse
Asynchronous
  Potentially faster
  Harder to analyze (more subtle, but more powerful!)
    Most of my research!
This course will look mostly at synchronous

## Slide 7: Storage Elements
Several types:
  Latch
  Flip-Flop
  Registers
  Addressable memories or banks of registers

## Slide 8: Basic Storage
Need feedback to hold a value
  Apply low or high once, and it will persist
Figure 3.1 Cross-coupled inverter pair

## Slide 9: Bistable Circuit Analysis
Consider 2 possible cases:
  Q = 0: then Q’ = 1 and Q = 0 (consistent)
  Q = 1: then Q’ = 0 and Q = 1 (consistent)
Bistable circuit stores 1 bit of state in the state variable, Q (or Q’)
But there are no inputs to control the state

## Slide 10: SR (set-reset) Latch
Basic storage made from gates
  A “1” on the input sets/resets the output
    ‘1’ on S sets the output Q to ‘1’
    ‘1’ on R resets the output Q to ‘0’
S & R both 0 in “resting” state
If both S & R are 1, Q and Q’ are both 0
  not a very useful case
Figure 3.3 SR latch schematic

## Slide 11: SR (set-reset) Latch
Bistable: Has two stable states

## Slide 12: SR Latch
Symbol

## Slide 13: SR Latch: Operation

## Slide 14: Latch
Similar, but dual
  made from NANDs
  A “0” on the input sets/resets the output
    ‘0’ on S’ sets the output Q to ‘1’
    ‘0’ on R’ resets the output Q to ‘0’

## Slide 15: SR Latch Summary
SR stands for Set/Reset Latch
  Stores one bit of state (Q)
Control what value is being stored with S, R inputs
  Set: Make the output 1 (S = 1, R = 0, Q = 1)
  Reset: Make the output 0 (S = 0, R = 1, Q = 0)
Behavior undesirable when:
  S = R = 1
    Q and Q’ are no longer complementary

## Slide 16: D Latch
Two modifications to SR latch
  Eliminate illegal state
    ensure that “set” and “reset” cannot be simultaneously asserted
    simply have one input called D (data)
      S is derived from D; R from D’
  Add a control input (CLK)
    to decide when the state should change
Figure 3.7 D latch: (a) schematic, (b) truth table, (c) symbol

## Slide 17: D Latch: Operation
When CLK = 0
  both S and R are 0
    previous value of output is held
When CLK = 1
  S=D, R=D’
    output is set to 1 if input D =1
    output is reset to 0 if input D =0
    output is updated to the value of input D
  NOTE: output will be continuously updated to D while CLK=1
Figure 3.7 D latch: (a) schematic, (b) truth table, (c) symbol

## Slide 18: D Latch: Transparency
Summary:
  When CLK = 0
    output is held
    we say: “D latch is opaque”
  When CLK = 1
    output follows the input
    we say: “D latch is transparent”
Figure 3.7 D latch: (a) schematic, (b) truth table, (c) symbol

## Slide 19: Effects of Transparency
Output of latch may feed back
  May cause/allow further state changes
  Behavior depends on actual gate delays
Want to change latch state only once
  Behavior should depend only on logical values

## Slide 20: Solution to Transparency: Flip-Flops
Flip-Flops:
  Ensure output changes only once per clock cycle
  Master-Slave construction
    Use a sequence of two latches

## Slide 21: D Flip-Flop (Master-Slave Flip-Flop)
Either Master or Slave is enabled, not both
  Master typically controlled by CLK’ and slave by CLK
    positive edge-triggered
    example on right
  Another common form has master controlled by CLK and slave by CLK’
    negative edge-triggered
Figure 3.8 D flip-flop: (a) schematic, (b) symbol, (c) condensed symbol

## Slide 22: D Flip-Flop: Operation
Edge-triggered
  when CLK goes from 0 to 1
    output Q is updated once to the input D value
  all other times, output is held
Why?
  master latch is transparent when CLK=0
    the last value of D that goes through to N1 is when CLK goes to 1
  slave latch is transparent when CLK=1
    the value that goes through is N1
    i.e., last value of D just before CLK goes to 1
Figure 3.8 D flip-flop: (a) schematic, (b) symbol, (c) condensed symbol

## Slide 23: Register
Simply multi-bit flip-flops
  N flip-flops stacked on top of each other = N-bit Register
Figure 3.9 A 4-bit register: (a) schematic and (b) symbol

## Slide 24: Adding More Control Inputs: Enable
Enable
  determines whether new data from input is captured on next clock edge, or ignored
  2 implementations (first one better)
    when EN=0, old value cycles back
    when EN=0, clock tick doesn’t reach the flip-flop
      messing with clock is messy!
Figure 3.10 Enabled flip-flop: (a, b) schematics, (c) symbol

## Slide 25: Adding More Control Inputs: Reset
Reset (synchronous)
  if RESET=1
    on next clock tick, stored value is changed to 0
  alternatively, if “Preset” or “Set” is used
    on next clock tick, stored value changed to 1
Figure 3.11 Synchronously resettable flip-flop: (a) schematic, (b, c) symbols

## Slide 26: Adding More Control Inputs: Reset
Asynchronous Reset
  stored value is reset immediately
  if RESET=1
    stored value is changed to 0
    does not wait for a clock tick
  requires modification to internal structure of latches of the flip-flop
    design not discussed in class, but may be a fun exercise for you!

## Slide 27: Latch and Flip-Flop comparison
Latch
  is transparent throughout the interval CLK=1
    all input changes during this time go through!
Flip-Flop
  only copies input to output at discrete instants
    last input D just before clock tick go through

## Slide 28: Counters
Increments on each clock edge
Used to cycle through numbers For example,
  000, 001, 010, 011, 100, 101, 110, 111, 000, 001…
  Not necessarily binary
Example uses:
  Digital clock displays
  Program counter

## Slide 29: Verilog design patterns for sequential logic

## Slide 30: Verilog for Sequential
One option is to use structural Verilog
  Can use latches and flip-flops from library
  And connect them using wires
Alternative: Use behavioral Verilog
  more productive to write behavioral description
  if you follow the templates provided, the synthesis tool can infer sequential logic

## Slide 31: Register (reg) Data Type
Like wire but value is retained over time
Often causes latch or FF to be synthesized
  but not always!
  sometimes the latch/FF is “optimized away” if not really necessary
  declaring reg is merely a suggestion to the compiler!
Examples:
reg state; // one flip-flop
reg [15:0] addr; // 16-bit register

## Slide 32: Always Block
Example
  always @ ( sensitivity list )
  statement;
Sensitivity list determines when statements are evaluated
  Could think of it as “statement is evaluated whenever one of values in sensitivity list changes”
Example next slide

## Slide 33: Synthesize a Flip-Flop
module flop (C, D, Q);
input C, D;
output Q;
reg Q; // Q needs 1 bit of storage
always @(posedge C) // here’s how Q is updated
begin
Q <= D;
end
endmodule
Behavioral description:
  always @(posedge C)  whenever C transitions from 0 to 1
  Q <= D;  output Q is updated to input D
negedge also possible

## Slide 34: Blocking vs. Non-blocking Assignment
Blocking assignments:
  Equal sign indicates blocking statements
  B = A;
  C = B;
  Result: new contents of B are in C, so all have contents of A
Non-blocking assignments:
  RHS of all <= lines within a begin-end block are evaluated in parallel, then assigned to LHS signals in parallel
  B <= A;
  C <= B;
  Result: new B is the value of A, but new C is the old B!

## Slide 35: This is Not Software!
Don’t assign to same reg in more than one always block
  The always blocks are concurrent
  Doesn’t make sense to set a reg from two different signals
For sequential logic: Use only non-blocking assignments
  you usually don’t mean one-by-one execution anyway
  yields the design pattern that is recognized by the compiler
    each reg on the LHS becomes a flip-flop/register
    each RHS becomes the input D to the reg
    sensitivity list (posedge clock) determines the clock signal
    enables/resets are also inferred if described

## Slide 36: Verilog template: Synchronous Reset
always @(posedge CLK)
begin
if (RESET)
state <= 0;
else
state <= D;
end
  OR
always @(posedge CLK)
state <= RESET? 0 : D;

## Slide 37: Verilog template: Counter
module counter(input clk, output [23:0] cnt);
reg [23:0] cnt;
always @ (posedge clk)
cnt <= cnt + 1’b1;
endmodule

## Slide 38: Simulation vs. Synthesis
If you don’t initialize regs in your circuits, simulator will complain
  many values will be X
Electronics will work OK
  each flipflop in actual circuit will “wake up” to a 0 or 1 value

## Slide 39: Verilog 2001 Syntax: Initialization
Can initialize regs at declaration
  reg onebit = 1’b0;
  reg [3:0] fourbits = 4’b1011;
  reg [23:0] cnt = 0; // widths default to 32 bits
  // and are padded
  // or truncated (keep LSBs)

## Slide 40: Topics
Today
  Looked at basic latches
  Flip-flops
  Verilog for sequential circuits
  Simple counter

## Slide 41: Read
Textbook Ch. 3.1-3.3 and Ch. 5.4.1 for today
  Ch. 3.4-3.5 for next class
Next Class: State Machines