## Slide 1: COMP541 Hierarchical Design & Verilog
Montek Singh
Aug 29, 2014

## Slide 2: Topics
Hierarchical Design
Verilog Primer and Advanced

## Slide 3: Design Hierarchy
Just like with large program, to design a large chip need hierarchy
Divide and Conquer
  To create, test, and also to understand
Block in a block diagram is equivalent to
  object in a programming language
  module in Verilog

## Slide 4: Hierarchy
Always make your design modular
  easier to read and debug
  easier to reuse
Before you write even one line of Verilog…
  …draw a picture
    black boxes
    boxes within boxes …

## Slide 5: Hierarchy Example: 4-bit Equality
Input: 2 vectors A(3:0) and B(3:0)
Output: One bit, E, which is 1 if A and B are bitwise equal, 0 otherwise

## Slide 6: Hierarchy Example: 4-bit Equality
Hierarchical design seems a good approach
One module/bit
Final module for E

## Slide 7: Design for MX module
Logic function is
  It is actually “not Equal”
  Can implement as

## Slide 8: Design for ME module
Final E is 1 only if all intermediate values are 0
So
And a design is

## Slide 9: MX
module mx(A, B, E);
input A, B;
output E;
assign E = (~A & B) | (A & ~B);
endmodule

## Slide 10: ME
module me(E, Ei);
input [3:0] Ei;
output E;
assign E = ~(Ei[0] | Ei[1] | Ei[2] | Ei[3]);
endmodule

## Slide 11: Top Level
module top(A, B, E);
input [3:0] A;
input [3:0] B;
output E;
wire [3:0] Ei;
mx m0(A[0], B[0], Ei[0]);
mx m1(A[1], B[1], Ei[1]);
mx m2(A[2], B[2], Ei[2]);
mx m3(A[3], B[3], Ei[3]);
me me0(E, Ei);
endmodule

## Slide 12: More on Verilog
A tutorial

## Slide 13: Change Topics to
Verilog
  Basic syntax and structure
Verilog test programs

## Slide 14: Constants in Verilog
Syntax
  [size][’radix]constant
Radix can be d, b, h, or o (default d)
Examples:
  assign Y = 10; // Decimal 10
  assign Y = ’b10; // Binary 10, decimal 2
  assign Y = ’h10; // Hex 10, decimal 16
  assign Y = 8’b0100_0011 // Underline ignored
Binary values can be 0, 1 (or x or z)

## Slide 15: Vector of Wires (Bus)
Denotes a set of wires
  input [1:0] S;
Syntax is [a : b]
  So this could be “[0:1] S”
  Order will matter when we make assignments with values bigger than one bit
  Or when we connect sets of wires
  Stick to the same ordering throughout design
NOTE: THIS IS NOT AN ARRAY!

## Slide 16: Conditional Assignment
Equality test
S == 2’b00
Assignment
assign Y = (S == 2’b00)? 1’b0: 1’b1;
  If true, assign 0 to Y
  If false, assign 1 to Y

## Slide 17: 4-to-1 Mux Truth Table-ish
module mux_4_to_1_dataflow(S, D, Y);
input [1:0] S;
input [3:0] D;
output Y;
assign Y = (S == 2'b00) ? D[0] :
(S == 2'b01) ? D[1] :
(S == 2'b10) ? D[2] :
(S == 2'b11) ? D[3] : 1'bx ;
endmodule

## Slide 18: Verilog for Decision Tree
module mux_4_to_1_binary_decision(S, D, Y);
input [1:0] S;
input [3:0] D;
output Y;
assign Y = S[1] ? (S[0] ? D[3] : D[2]) :
(S[0] ? D[1] : D[0]) ;
endmodule

## Slide 19: Binary Decisions
If S[1] == 1, branch one way
assign Y = S[1] ? (S[0] ? D[3] : D[2])
  and decide Y = either D[2] or D[3] based on S[0]
Else
: (S[0] ? D[1] : D[0]) ;
  decide Y is either D[2] or D[3] based on S[0]
Notice that conditional test is for ‘1’ condition like C

## Slide 20: Instance Port Names
Module
module modp(output C, input A);
Ports referenced as
modp i_name(conC, conA)
Also as
modp i_name(.A(conA), .C(conC));

## Slide 21: Parameter
Used to define constants
parameter SIZE = 16;
Or, for parameters local to a module:
localparam SIZE = 16;
More on these later

## Slide 22: Internal Variables
Internals = those that are not inputs/outputs
  declare them as wire or reg
    depending on whether they are combinational or state holding
module fulladder(input a, b, cin, output s, cout);
wire p, g; // internal
assign p = a ^ b;
assign g = a & b;
assign s = p ^ cin;
assign cout = g | (p & cin);
endmodule

## Slide 23: Bitwise Operators (we have used)
module gates(input [3:0] a, b,
output [3:0] y1, y2, y3, y4, y5);
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR
endmodule

## Slide 24: Comments
// single line comment
/*…*/ multiline comment

## Slide 25: Reduction Operators (&)
Unary operator that works on all of the bits
  E.g., AND all of the bits of a word together
  Gives a 1-bit result
module and8(input [7:0] a,
output y);
assign y = &a;
// &a is much easier to write than
// assign y = a[7] & a[6] & a[5] & a[4] &
// a[3] & a[2] & a[1] & a[0];
endmodule

## Slide 26: Reduction Operators (|, ~|, ~&, ^, ~^, ^~)
Several others (see online reference)
  | = OR all the bits together
  ~| = NOR all the bits together
  ~& = NAND all the bits together
  ^ = XOR all the bits together
  ~^, ^~ = XNOR all the bits together

## Slide 27: Operator Precedence
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, XOR
?: | ternary operator
Highest
Lowest

## Slide 28: Numbers
Format: N’Bvalue
  N = number of bits, B = base
  N’B is optional but recommended (default is decimal)
  whenever in doubt, specify the # of bits
Number | # Bits | Base | Decimal Equivalent | Value Stored
3’b101 | 3 | binary | 5 | 101
’b11 | unsized | binary | 3 | 00…0011
8’b11 | 8 | binary | 3 | 00000011
8’b1010_1011 | 8 | binary | 171 | 10101011
3’d6 | 3 | decimal | 6 | 110
6’o42 | 6 | octal | 34 | 100010
8’hAB | 8 | hexadecimal | 171 | 10101011
42 | Unsized | decimal | 42 | 00…0101010

## Slide 29: Bit Manipulations: splitting bits off
module mux2_8(input [7:0] d0, d1,
input s,
output [7:0] y);
mux2 lsbmux(d0[3:0], d1[3:0], s, y[3:0]);
mux2 msbmux(d0[7:4], d1[7:4], s, y[7:4]);
endmodule
Synthesis:
Verilog:

## Slide 30: Bit Manipulations: packing bits
assign y = {a[2:1], {3{b[0]}}, a[0], 6’b100_010};
// if y is a 12-bit signal, the above statement produces:
y = a[2] a[1] b[0] b[0] b[0] a[0] 1 0 0 0 1 0
// underscores (_) are used for formatting only to make it easier to read. Verilog ignores them.

## Slide 31: Verilog for Simulation and Testing

## Slide 32: Verilog for Simulation vs. Synthesis
Simulation
  you describe the circuit in Verilog
  simulate it
  good for
    testing whether your conceptual design works before your spend $$ getting it fabricated in silicon
Synthesis
  you describe the behavior in Verilog
  use a compiler to “compile” it into a circuit
  good for
    describing large-scale complex systems without every manually building them
    the “compiler” translates it into a circuit for you!

## Slide 33: Verilog for Simulation vs. Synthesis
Remember:
  for simulation: Verilog provides many more language constructs and features
  for synthesis: Verilog supports only a subset of the language that makes sense!
    called “synthesizable subset”

## Slide 34: ISE
Make Verilog Test Fixture
Will create a wrapper (a module)
  Instantiating your circuit
  It is called UUT (unit under test)
You then add your test code

## Slide 35: Test fixtures
Testing your circuit using a Verilog test fixture
Module
module lab1_part1(
input A, B, Cin,
output Sum);
Ports referenced as
lab1_part1 uut(X, Y, Z, T)
Also as
lab1_part1 uut(.A(X), .B(Y), .Sum(T), .Cin(Z))
Circuit to
be tested
(“uut”)
Stimulus:
initial begin
…
end
inputs
outputs
Verilog test fixture

## Slide 36: Module and Instance UUT
module syn_adder_for_example_v_tf();
// DATE: 21:22:20 01/25/2004
// ...Bunch of comments...
...
// Instantiate the UUT
syn_adder uut (
.B(B),
.A(A),
.C0(C0),
.S(S),
.C4(C4)
);
...
endmodule

## Slide 37: Reg
It will create storage for the inputs to the UUT
// Inputs
reg [3:0] B;
reg [3:0] A;
reg C0;
The keyword reg means “register”
  Usually implies a storage element is created
    Sometimes may be “optimized away” to create combinational logic

## Slide 38: Wires for Outputs
Specify bus size (for multibit wires)
// Outputs
wire [3:0] S;
wire C4;

## Slide 39: Begin/End
Verilog uses begin and end for block
  instead of curly braces

## Slide 40: Initial
Initial statement runs when simulation begins
initial
begin
B = 0;
A = 0;
C0 = 0;
end

## Slide 41: Procedural assignment
Why no “assign”?
  Because it is not a continuous assignment
  It is a one-off assignment!
  And here we use blocking assignments
    So everything happens in sequence rather than in parallel
      Good for describing test fixtures, but not good for synthesis!

## Slide 42: Initialize in Default Test File
The test file can specify the initial values of inputs to your circuit
// Initialize Inputs
initial begin
B = 0;
A = 0;
C0 = 0;
end

## Slide 43: What to Add?
Need to make simulation time pass
Use # command for skipping time
  time increases by 5 units when you encounter #5
Example (note no semicolon after #50)
initial
begin
B = 0;
#10;
#50 B = 1;
end

## Slide 44: For
Can use for loop in initial statement block
initial
begin
for(i=0; i < 5; i = i + 1)
begin
#50 B = i;
end
end

## Slide 45: Integers
Can declare for loop control variables
  Will not synthesize, as far as I know
  integer i;
  integer j;
Can copy to input regs
  Be careful with signed vs. unsigned quantities

## Slide 46: There are also
While
Repeat
Forever

## Slide 47: Timescale
Need to tell simulator what time scale to use
Place at top of test fixture
`timescale 1ns/10ps
  the first number (1ns) is the unit for time
  the second number (10ps) is the precision at which time is maintained (e.g., 5.01 ns)

## Slide 48: System Tasks
Tasks for the simulator
$stop – end the simulation
$display – like C printf
$monitor – prints automatically when arguments change (example next)
$time – Provides value of simulated time

## Slide 49: Monitor
// set up monitoring
initial
begin
$monitor(“At time %d: A=%b ,B=%b\n", $time, A, B);
end
// These statements conduct the actual test
initial
begin
Code...
end