## Slide 1
1801, Joseph Marie Jacquard
Jacquard Loom and punch cards to program it.
(George H. Williams, photos from Wikipedia)
Slide courtesy Anselmo Lastra

## Slide 2: COMP 740: Computer Architecture and Implementation
Montek Singh
Aug 24, 2016
Lecture 1

## Slide 3: What is “Computer Architecture”?
Term coined by Fred Brooks and colleagues at IBM:
“…the structure of a computer that a machine language programmer
must understand to write a correct (timing independent) program for that
machine.”
Amdahl, Blaauw, and Brooks, 1964
“Architecture of the IBM System 360”,
IBM Journal of Research and Development
Do you know about System 360 family?

## Slide 4: What is “Computer Architecture”?
Several years ago, the term computer architecture often referred only to instruction set design. Other aspects of computer design were called implementation, often insinuating that implementation is uninteresting or less challenging.
We believe this view is incorrect. The architect’s or designer’s job is much more than instruction set design, and the technical hurdles in the other aspects of the project are likely more challenging than those encountered in instruction set design.
- Patterson & Hennessy
Term used differently by Hennessy and Patterson (our textbook)
  includes much implementation

## Slide 5: Outline
Course Information
  Logistics
  Grading
  Syllabus
  Course Overview
Technology Trends
  Moore's Law

## Slide 6: Course Information (1)
Time and Place
  Mon/Wed 1:25-2:40 pm, FB007
Instructor
  Montek Singh
  montek@cs.unc.edu
  FB234, 919-590-6132
  Office hours: TBA
Course Web Page
  Linked from mine: http://www.cs.unc.edu/~montek

## Slide 7: Course Information (2)
Prerequisites
  Undergrad comp. org. (Comp411) and digital logic (Comp541)
  I assume you know the following topics
    CPU: ALU, control unit, registers, buses, memory management
    Control Unit: register transfer language, implementation, hardwired and microprogrammed control
    Memory: address space, memory capacity
    I/O: CPU-controlled (polling, interrupt), autonomous (DMA)
    Pipelining (at least an overview)
  Representative books (available in Brauer Library)
    Patterson & Hennessy: Computer Organization and Design: The Hardware/Software Interface. Morgan Kaufmann Publishers.
    Harris & Harris: Digital Design and Computer Architecture, 2nd ed. (July 2012), Morgan Kaufmann Publishers.

## Slide 8: Course Information (3)
Textbook
  Hennessy & Patterson: Computer Architecture: A Quantitative Approach (5th edition), Morgan Kaufmann Publishers, Sep 2011
    available at amazon.com, bn.com…
  Quite different from earlier eds.: more on multiprocessing (multicore)
Notes: We will cover the green material very quickly, the orange material somewhat quickly, and the red material in great detail.
The additional readings are important. Learning to read technical papers is an important skill that you need to pick up in graduate school.

## Slide 9: Course Information (4)
Textbook (contd.)
  We will cover the following material:
    Fundamentals of Computer Design (Chapter 1)
    Instruction Set Principles and Examples (App A & K)
    Memory-Hierarchy Design (App B & Chapter 2)
    Pipelining: Basic and Intermediate Concepts (App C)
    Instruction-Level Parallelism (Chapter 3)
    Data-Level Parallelism (Chapter 4)
    Thread-Level Parallelism (Chapter 5)
    Storage Systems (App D)
    On-Chip Networks (selected readings)
    Emerging Technologies of Computation (selected readings)
Additional readings/papers may be handed out
  e.g., case studies on the last two topics above
Notes: We will cover the green material very quickly, the orange material somewhat quickly, and the red material in great detail.
The additional readings are important. Learning to read technical papers is an important skill that you need to pick up in graduate school.

## Slide 10: Course Information (5)
Grading
  30% homework assignments
  10% quizzes
  20% midterm exam
  30% final exam
  10% class presentation
    e.g., present a survey or case study on multicore
    e.g., present a paper on DNA-based computing technologies
Assignments are due at beginning of class on due date
  Late assignments: penalty=10%/day or part thereof
Honor Code is in effect: for all homework/exams/projects
  encouraged to discuss ideas/concepts with others
  work handed in must be your own

## Slide 11: What is in COMP 740 for me?
Understand modern computer architecture so you can:
  Write better programs
    Understand the performance implications of algorithms, data structures, and programming language choices
  Write better compilers
    Modern computers need better optimizing compilers and better programming languages
  Write better operating systems
    Need to re-evaluate the current assumptions and tradeoffs
    Example: fully exploit multicore/manycore architectures
  Design better computer architectures
    There are still many challenges left
    Example: how to design efficient multicore architectures
  Satisfy the Distribution Requirement

## Slide 12: Acknowledgements
Material for this class taken from
  My old COMP 206 course notes
  Prof. Anselmo Lastra's 740 slides
  Prof. Sid Chatterjee's old 206 slides
  Professor David Patterson's (Berkeley) course notes
  Textbook web site
  Other websites

## Slide 13: Computer Architecture Topics
Pipelining, Hazard Resolution,
Superscalar, Reordering,
Prediction, Speculation
Addressing,
Protection,
Exception Handling
L1 Cache
L2 Cache
DRAM
Disks, Tape
Coherence,
Bandwidth,
Latency
Emerging Technologies
Interleaving
Bus protocols
RAID
VLSI
Input/Output and Storage
Memory
Hierarchy
Pipelining
Instruction-Level Parallelism
Multiprocessing/Multicore
Instruction Set Architecture

## Slide 14: Trends of 2000-2015
Technology
  Very large dynamic RAM: 256 Mbits to 4Gb and beyond
  Large fast static RAM: 16 MB, 5ns
Complete systems on a chip
  100+ million to 1+ billion transistors
Parallelism
  Superscalar, Superpipelined, Vector, Multiprocessors?
  Processor Arrays?
  Multicore/manycore!
Special-Purpose Architectures
  GPU's, mp3 players, nanocomputers …
Reconfigurable Computers?
  Wearable computers

## Slide 15: Trends of 2000-2015
Low Power
  Over 50% of computing devices portable now (!)
  Hand held communicators
  Performance per watt, battery life
  Transmeta
  Asynchronous (clockless) design
Communication (I/O)
  Many applications I/O limited, not computation
  Computation scaling, but memory, I/O bandwidth not keeping pace
Multimedia
  New interface technologies
  Video, speech, handwriting, virtual reality, …

## Slide 16: Diversion: Clocked Digital Design
Most current digital systems are synchronous:
  Clock: a global signal that paces operation of all components
clock
Benefit of clocking: enables discrete-time representation
  all components operate exactly once per clock tick
  component outputs need to be ready by next clock tick
    allows “glitchy” or incorrect outputs between clock ticks

## Slide 17: Microelectronics Trends
Current and Future Trends: Significant Challenges
  Large-Scale “Systems-on-a-Chip” (SoC)
    100 Million ~ 1 Billion transistors/chip
  Very High Speeds
    multiple GigaHertz clock rates
  Explosive Growth in Consumer Electronics
    demand for ever-increasing functionality …
    … with very low power consumption (limited battery life)
  Higher Portability/Modularity/Reusability
    “plug 'n play” components, robust interfaces

## Slide 18: Alternative Paradigm: Asynchronous Design
Digital design with no centralized clock
Synchronization using local “handshaking”
Asynchronous Benefits:
  Higher Performance: not limited by slowest component
  Lower Power: zero clock power; inactive parts consume little power
  Reduced Electromagnetic Noise: no clock spikes [e.g., Philips pagers]
  Greater Modularity: variable-speed interfaces; reusable components
Asynchronous System
(Distributed Control)
handshaking
interface
Synchronous System
(Centralized Control)
clock

## Slide 19: Trends: Performance
Era of the microprocessor.
Increases due to transistors
and architectural improvements
Move to multi-processor
RISC

## Slide 20: Trends: Clock speed
Figure 1.11 Growth in clock rate of microprocessors in Figure 1.1. Between 1978 and 1986, the clock rate improved less than 15% per year while performance improved by 25% per year. During the “renaissance period” of 52% performance improvement per year between 1986 and 2003, clock rates shot up almost 40% per year. Since then, the clock rate has been nearly flat, growing at less than 1% per year, while single processor performance improved at less than 22% per year.

## Slide 21: Performance
Increase by 2002 was much faster than would have been due to fabrication tech (e.g. 0.13 micron) alone
What has slowed the trend?
  Note what is really being built
    A commodity device!
    So cost is very important
  Problems
    Amount of heat that can be removed economically
    Limits to instruction level parallelism
    Memory latency

## Slide 22: Moore's Law
What is Moore’s Law?
Originally: Number of transistors on a chip
  at the lowest cost/component
It's not quite clear what it really is 
  Moore's original paper, doubling yearly
    Didn't make it in 1975
  Often quoted as doubling every 18 months
  Sometimes as doubling every two years
Moore's article worth reading
  http://download.intel.com/research/silicon/moorespaper.pdf

## Slide 23: Quantitative Principles of Computer Design
Execution time
Response time
Latency
Performance
Rate of producing results
Throughput
Bandwidth

## Slide 24: Quick Look: Classes of Computers
Used to be
  mainframe,
  mini, and
  micro
Now
  Desktop
    Price/performance, single app, graphics
  Server
    Reliability, scalability, throughput
  Embedded
    Not only “toasters”, but also cell phones, etc.
    Cost, power, real-time performance
  Mobile
    smartphones, tablets, fitness devices, etc.

## Slide 25: Chip Performance
Based on a number of factors
  Feature size (or “technology” or “process”)
    Determines transistor & wire density
    Used to be measured in microns, now nanometers
    Currently: 90 nm, 65 nm, 45 nm, even 22 nm
  Die size
  Device speed
Note section on wires in textbook
  Thin wires  more resistance and capacitance
  Wire delay scales poorly
    simply making transistors faster is not sufficient anymore
    managing connectivity is the big challenge now

## Slide 26: ITRS
International Technology Roadmap for Semiconductors
  http://www.itrs2.net/
  An industry consortium
  predicts trends
  take a look at the yearly report on their website
    take a few minutes to skim the “executive summary”

## Slide 27: ITRS Predictions (2012 update)

## Slide 28: Aside: Ray Kurzweil
Kurzweil: futurist, author
  Book in 2005: “The Singularity is Near”
    Movie in 2010
    Predicts singularity around 2045
[From Wikipedia]
The technological singularity, or simply the singularity, is a hypothetical moment in time when artificial intelligence will have progressed to the point of a greater-than-human intelligence, radically changing civilization, and perhaps human nature. Since the capabilities of such an intelligence may be difficult for a human to comprehend, the technological singularity is often seen as an occurrence (akin to a gravitational singularity) beyond which the future course of human history is unpredictable or even unfathomable.

## Slide 29: Trends
Now let’s look at trends in
  Bandwidth (Throughput) vs. Latency
  Power
  Cost
  Dependability
  Performance

## Slide 30: Bandwidth vs. Latency
What is “bandwidth”?
  or “throughput”
  total amount of work done per time
  e.g.: MB/sec for disk or network transfer
  e.g.: billions of instructions/sec executed by CPU
What is “latency”?
  or “response time”
  time between start and completion
  e.g.: milliseconds for a disk access
  e.g.: time lag for video game to respond to user input
Very important to understand distinction
  see textbook, pp. 18-19

## Slide 31: Bandwidth vs. Latency
These metrics apply to various components
  microprocessor, memory, disk, network
  latency improved 6X to 80X
  bandwidth improved about 300X to 25,000X
Textbook Figure 1.9 Log–log plot of bandwidth and latency milestones.
Note that latency improved 6X to 80X while bandwidth improved about 300X to 25,000X.
CPU high,
Memory low (“Memory Wall”)

## Slide 32: Bandwidth vs. Latency
Bandwidth improves much faster than latency
  In the time that bandwidth doubles, latency improves by no more than a factor of 1.2 to 1.4
  (and capacity improves faster than bandwidth)
Or:
  bandwidth improves by more than the square of the improvement in latency
  what could be the reason for bandwidth to improve faster than latency?
    easier to exploit parallelism of more transistors to improve bandwidth
    improvements to latency limited by delays, sequentiality, etc.

## Slide 33: Why Less Improvement?
Moore’s Law helps bandwidth
  Longer distance for signal to travel, so longer latency
  Which offsets faster transistors
Distance limits latency
  Speed of light lower bound
Bandwidth sells
  Capacity, processor “speed” and benchmark scores
Latency can help bandwidth
  Often bandwidth is increased by adding latency
OS introduces latency

## Slide 34: Techniques to Ameliorate
Caching
  Use capacity (“bandwidth”) to reduce average latency
Replication
  Again, leverage capacity
Prediction
  Use extra processing transistors to pre-fetch
  Maybe also to recompute instead of fetch

## Slide 35: Trends
Now let’s look at trends in
  Bandwidth vs. Latency
  Power
  Cost
  Dependability
  Performance

## Slide 36: Power
For CMOS chips, traditional dominant energy consumption has been in switching transistors, called dynamic power
For mobile devices, energy is better metric:
For fixed task, slowing clock rate reduces power, not energy
Capacitive load a function of number of transistors connected to output and of technology, which determines capacitance of wires and transistors
Dropping voltage helps both, moved from 5V to 1V
Clock gating

## Slide 37: Power
Intel 80386 consumed ~ 2 W
3.3 GHz Intel Core i7 consumes 130 W
Heat must be dissipated from 1.5 x 1.5 cm chip
This is the limit of what can be cooled by air

## Slide 38: How to reduce power?
Several techniques
  Design circuits to be energy efficient
    some clever techniques avoid wasteful energy consumption
    other techniques adversely affect performance
  Reduce clock rate
    frequency scaling
  Reduce voltage and clock rate
    voltage-frequency scaling
    done dynamically, in response to demand
  Clock gating and voltage gating
    turn off parts of the system
    e.g., turn off unneeded cores, put memory/disks in idle

## Slide 39: Voltage and Frequency Scaling
Figure 1.12 Energy savings for a server using an AMD Opteron microprocessor, 8 GB of DRAM, and one ATA disk.
At 1.8 GHz, the server can only handle up to two-thirds of the workload without causing service level violations, and, at 1.0 GHz, it can only safely handle one-third of the workload. (Figure 5.11 in Barroso and Hölzle [2009].)

## Slide 40: Example: Reducing Power
Suppose 15% reduction in voltage results in a 15% reduction in frequency. What is impact on dynamic power?

## Slide 41: Trends in Power
Because leakage current flows even when a transistor is off, now static power important too
Leakage current increases in processors with smaller transistor sizes
Increasing the number of transistors increases power even if they are turned off
In 2006, goal for leakage was 25% of total power consumption; high performance designs at 40%
Very low power systems even gate voltage to inactive modules to control loss due to leakage

## Slide 42: Trends
Now let’s look at trends in
  Bandwidth vs. Latency
  Power
  Cost
  Dependability
  Performance

## Slide 43: Cost of Integrated Circuits
Dingwall’s Equation

## Slide 44: Explanations
Second term in “Dies per wafer”
corrects for the rectangular dies
near the periphery of round wafers
“Die yield” assumes a simple empirical
model: defects are randomly distributed
over the wafer, and yield is inversely
proportional to the complexity of the
fabrication process (indicated by a)
a=3 for modern processes implies that
cost of die is proportional to (Die area)4

## Slide 45: Real World Examples
“Revised Model Reduces Cost Estimates”, Linley Gwennap, Microprocessor Report 10(4), 25 Mar 1996

## Slide 46: Trends
Now let’s look at trends in
  Bandwidth vs. Latency
  Power
  Cost
  Dependability
  Performance

## Slide 47: Dependability
When is a system operating properly?
Infrastructure providers now offer Service Level Agreements (SLA) to guarantee that their networking or power service would be dependable
Systems alternate between 2 states of service with respect to an SLA:
  Service accomplishment, where the service is delivered as specified in SLA
  Service interruption, where the delivered service is different from the SLA
Failure = transition from state 1 to state 2
Restoration = transition from state 2 to state 1

## Slide 48: Definitions
Module reliability = measure of continuous service accomplishment (or time to failure)
Two key metrics:
  Mean Time To Failure (MTTF) measures Reliability
  Failures In Time (FIT) = 1/MTTF, the rate of failures
    Traditionally reported as failures per billion hours of operation
Derived metrics:
  Mean Time To Repair (MTTR) measures Service Interruption
    Mean Time Between Failures (MTBF) = MTTF+MTTR
  Module availability measures service as alternate between the 2 states of accomplishment and interruption (number between 0 and 1, e.g. 0.9)
    Module availability = MTTF / ( MTTF + MTTR)

## Slide 49: Example -- Calculating Reliability
If modules have exponentially distributed lifetimes (age of module does not affect probability of failure), overall failure rate is the sum of failure rates of the modules
Calculate FIT and MTTF for 10 disks (1M hour MTTF per disk), 1 disk controller (0.5M hour MTTF), and 1 power supply (0.2M hour MTTF):
Solution next
1M hours = 114 years!
0.2M hours = 22 years!

## Slide 50: Solution
If modules have exponentially distributed lifetimes (age of module does not affect probability of failure), overall failure rate is the sum of failure rates of the modules
Calculate FIT and MTTF for 10 disks (1M hour MTTF per disk), 1 disk controller (0.5M hour MTTF), and 1 power supply (0.2M hour MTTF):
less than 7 years!

## Slide 51: Trends
Now let’s look at trends in
  Bandwidth vs. Latency
  Power
  Cost
  Dependability
  Performance

## Slide 52: First, What is Performance?
The starting point is universally accepted
  “The time required to perform a specified amount of computation is the ultimate measure of computer performance”
How should we summarize (reduce to a single number) the measured execution times (or measured performance values) of several benchmark programs?
  Two properties
    A single-number performance measure for a set of benchmarks expressed in units of time should be directly proportional to the total (weighted) time consumed by the benchmarks.
    A single-number performance measure for a set of benchmarks expressed as a rate should be inversely proportional to the total (weighted) time consumed by the benchmarks.
from “Characterizing Computer Performance with a Single Number”, J. E. Smith, CACM, October 1988, pp. 1202-1206

## Slide 53: Quantitative Principles of Computer Design
Performance is in units of things per second
  So bigger is better
What if we are primarily concerned with response time?
Execution time
Response time
Latency
Performance
Rate of producing results
Throughput
Bandwidth

## Slide 54: Performance: What to measure?
What about just MIPS and MFLOPS?
Usually rely on benchmarks vs. real workloads
Older measures were
  Kernels or
  Small programs designed to mimic real workloads
Whetstone, Dhrystone
http://www.netlib.org/benchmark
Note LINPACK and Top500

## Slide 55: MIPS
Machines with different instruction sets?
Programs with different instruction mixes?
Uncorrelated with performance
  Marketing metric
“Meaningless Indicator of Processor Speed”

## Slide 56: MFLOP/s
Popular in supercomputing community
Often not where time is spent
Not all FP operations are equal
  “Normalized” MFLOP/s
Can magnify performance differences
  A better algorithm (e.g., with better data reuse) can run faster even with higher FLOP count

## Slide 57: Peak Performance
Figure 1.20 Percentage of peak performance for four programs on four multiprocessors scaled to 64 processors. The Earth Simulator and X1 are vector processors (see Chapter 4 and Appendix G). Not only did they deliver a higher fraction of peak performance, but they also had the highest peak performance and the lowest clock rates. Except for the Paratec program, the Power 4 and Itanium 2 systems delivered between 5% and 10% of their peak. From Oliker et al. [2004].

## Slide 58: Benchmarks
To increase predictability, collections of benchmark applications, called benchmark suites, are popular
SPECCPU: popular desktop benchmark suite
  CPU only, split between integer and floating point programs
  SPECint2000 has 12 integer, SPECfp2000 has 14 integer pgms
  SPECCPU2006 was announced Spring 2006
  SPECSFS (NFS file server) and SPECWeb (WebServer) added as server benchmarks
  www.spec.org
Transaction Processing Council measures server performance and cost-performance for databases
  TPC-C Complex query for Online Transaction Processing
  TPC-H models ad hoc decision support
  TPC-W a transactional web benchmark
  TPC-App application server and web services benchmark

## Slide 59: SPEC2006 Programs

## Slide 60: How to Summarize Performance?
Arithmetic average of execution times??
  But they vary in basic speed, so some would be more important than others in arithmetic average
Could add weights per program, but how to pick weight?
  Different companies want different weights for their products
SPECRatio: Normalize execution times to reference computer, yielding a ratio proportional to performance =
  time on reference computer / time on computer being rated
  Spec uses an older Sun machine as reference

## Slide 61: Ratios
If program SPECRatio on Computer A is 1.25 times bigger than Computer B, then
Note that when comparing 2 computers as a ratio, execution times on the reference computer drop out, so choice of reference computer is irrelevant

## Slide 62: Review: Different means

## Slide 63: Geometric Mean
Since ratios, proper mean is geometric mean (SPECRatio unitless, so arithmetic mean meaningless)
Geometric mean of the ratios is the same as the ratio of the geometric means
Ratio of geometric means = Geometric mean of performance ratios  choice of reference computer is irrelevant!
These two points make geometric mean of ratios attractive to summarize performance

## Slide 64: Different Take
Smith (CACM 1988, see references) takes a different view on means
First let’s look at an example

## Slide 65: Rates
Change to MFLOPS and also look at different means

## Slide 66: Avoid the Geometric Mean?
If benchmark execution times are normalized to some reference machine, and means of normalized execution times are computed, only the geometric mean gives consistent results no matter what the reference machine is
  This has led to declaring the geometric mean as the preferred method of summarizing execution time (e.g., SPEC)
Smith’s comments
  “The geometric mean does provide a consistent measure in this context, but it is consistently wrong.”
  “If performance is to be normalized with respect to a specific machine, an aggregate performance measure such as total time or harmonic mean rate should be calculated before any normalizing is done. That is, benchmarks should not be individually normalized first.”
  He advocates using time, or normalizing after taking mean

## Slide 67: Variability
Does a single mean summarize performance of programs in benchmark suite?
Can decide if good predictor by characterizing variability of distribution using standard deviation
Like geometric mean, geometric standard deviation is multiplicative rather than arithmetic
Can simply take the logarithm of SPECRatios, compute the standard mean and standard deviation, and then take the exponent to convert back:

## Slide 68: Form of Standard Deviation
Standard deviation is more informative if we know distribution has a standard form
  bell-shaped normal distribution, whose data are symmetric around mean
  lognormal distribution, where logarithms of data--not data itself--are normally distributed (symmetric) on a logarithmic scale
For a lognormal distribution, we expect that
68% of samples fall in range
95% of samples fall in range

## Slide 69: Example (1/2)
GM and multiplicative StDev of SPECfp2000 for Itanium 2

## Slide 70: Example (2/2)
GM and multiplicative StDev of SPECfp2000 for AMD Athlon

## Slide 71: Comments
Standard deviation of 1.98 for Itanium 2 is much higher-- vs. 1.40--so results will differ more widely from the mean, and therefore are likely less predictable
Falling within one standard deviation:
  10 of 14 benchmarks (71%) for Itanium 2
  11 of 14 benchmarks (78%) for Athlon
Thus, the results are quite compatible with a lognormal distribution (expect 68%)

## Slide 72: Next Lecture
Principles of Computer Design
Amdahl’s Law

## Slide 73: Readings/References
Gordon Moore’s paper
  http://www.intel.com/pressroom/kits/events/moores_law_40th/index.htm
  http://download.intel.com/museum/Moores_Law/Articles-Press_Releases/Gordon_Moore_1965_Article.pdf
Paper on which latency section is based
  Patterson, D. A. 2004. Latency lags bandwidth. Commun. ACM 47, 10 (Oct. 2004), 71-75.
“Characterizing Computer Performance with a Single Number”, J. E. Smith, CACM, October 1988, pp. 1202-1206