## Slide 1: COMP 740: Computer Architecture and Implementation
Montek Singh
Oct 31, 2016
Topic: Instruction-Level Parallelism
(Multiple-Issue, Speculation)

## Slide 2: Outline
Multiple-Issue Architectures
  Superscalar processors
  VLIW (very long instruction word) processors
Scheduling
  Statically scheduled (using compiler techniques)
  Dynamically scheduled (using variants of Tomasulo’s alg.)
Reading: HP5, Sections 3.6-3.10

## Slide 3: Multiple Issue
Eliminating data and control stalls can achieve CPI of 1
Can we decrease CPI below 1?
  Not if we issue only one instruction per clock cycle
Multiple-issue processors allow multiple instructions to issue in a clock cycle
  Superscalar: issue varying numbers of instructions per clock
    Statically scheduled by compiler, OR
    Dynamically scheduled by hardware
  VLIW: issue fixed number of instructions per clock
    Statically scheduled by compiler
Examples
  Superscalar: IBM PowerPC, Sun SuperSPARC, DEC Alpha, HP 8000
    Intel Core series: 4-way superscalar
  VLIW: Intel/HP Itanium

## Slide 4: A Superscalar Version of MIPS
Two instructions can be issued per clock cycle
  One can be load/store/branch/integer operation
  Other can be any FP operation
Need to fetch and decode 64 bits per cycle
  Instructions paired and aligned on 64-bit boundary
  Integer instruction appears first
Dynamic issue
  First instruction issues if independent and satisfies other criteria
  Second instruction issues only if first one does, and is independent and satisfies similar criteria
Limitation
  One-cycle delay for loads and branches now turns into three-instruction delay!
    … because instructions are now squeezed closer together

## Slide 5: Simple Superscalar MIPS

## Slide 6: Performance of Static Superscalar
LOOP:
L.D F0, 0(R1)
ADD.D F4, F0, F2
S.D 0(R1), F4
SUBI R1, R1, 8
BNEZ R1, LOOP
LOOP: L.D F0, 0(R1)
L.D F6, -8(R1)
L.D F10, -16(R1) ADD.D F4, F0, F2
L.D F14, -24(R1) ADD.D F8, F6, F2
L.D F18, -32(R1) ADD.D F12, F10, F2
S.D 0(R1), F4 ADD.D F16, F14, F2
S.D -8(R1), F8 ADD.D F20, F18, F2
S.D -16(R1), F12
SUBI R1, R1, 40
S.D 16(R1), F16
BNEZ R1, LOOP
S.D 8(R1), F20
Assumptions: L.D takes 2 cycles, ADD.D takes 3
Loop unrolled five times and scheduled statically
  6 cycles per element in original scheduled code
  2.4 cycles per element in superscalar code (2.5x)
  Loop unrolling gets us from 6 to 3.5 cycles per element (1.7x)
  Superscalar execution from 3.5 to 2.4 cycles per element (1.5x)

## Slide 7: Multiple-Issue with Dynamic Scheduling
Extend Tomasulo’s algorithm
  support issuing 2 instr/cycle: 1 integer, 1 FP
Simple approach:
  separate Tomasulo Control for Integer and FP units:
    one set of reservation stations for Integer unit and one for FP unit
How to do instruction issue with two instructions and keep in-order instruction issue for Tomasulo?
  issue logic runs in one-half clock cycle
  can do two in-order issues in one clock cycle

## Slide 8: Performance of Dynamic Superscalar
Iter. no. Instructions Issues Executes Writes result
(clock-cycle number)
1 L.D F0,0(R1) 1 2 4
1 ADD.D F4,F0,F2 1 5 8
1 S.D 0(R1),F4 2 9
1 SUBI R1,R1,8 3 4 5
1 BNEZ R1,LOOP 4 5
2 L.D F0,0(R1) 5 6 8
2 ADD.D F4,F0,F2 5 9 12
2 S.D 0(R1),F4 6 13
2 SUBI R1,R1,8 7 8 9
2 BNEZ R1,LOOP 8 9
4 clocks per iteration

## Slide 9: Limits of Superscalar
While Integer/FP split is simple to implement, we get CPI of 0.5 only for programs with:
  Exactly 50% FP operations
  No hazards
If more instructions issue at same time, greater difficulty of decode and issue
  Even 2-scalar machine has to do a lot of work
    Examine 2 opcodes
    Examine 6 register specifiers
    Decide if 1 or 2 instructions can issue
    If 2 are issuing, issue them in-order

## Slide 10: Modern Superscalar
4-6 instructions/clock
  Intel Core series (i3/i5/i7): 4-way superscalar
Issue in fraction of clock steps, and also include logic to deal with dependencies
Need to complete (i.e., write results of) multiple instructions per clock as well

## Slide 11: Very Long Instruction Word (VLIW)
VLIW: trade off instruction space for simple decoding
  The long instruction word has room for many operations
  By definition, all the operations the compiler puts in the long instruction word can execute in parallel
  E.g., 2 integer operations, 2 FP operations, 2 memory references, 1 branch
    16 to 24 bits per field => 7*16 or 112 bits to 7*24 or 168 bits wide
  Need very sophisticated compiling technique …
    … that schedules across several branches

## Slide 12: Loop Unrolling in VLIW
Memory Memory FP FP Int. op/ Clock reference 1 reference 2 operation 1 op. 2 branch
L.D F0,0(R1) L.D F6,-8(R1) 1
L.D F10,-16(R1) L.D F14,-24(R1) 2
L.D F18,-32(R1) L.D F22,-40(R1) ADD.D F4,F0,F2 ADD.D F8,F6,F2 3
L.D F26,-48(R1) ADD.D F12,F10,F2 ADD.D F16,F14,F2 4
ADD.D F20,F18,F2 ADD.D F24,F22,F2 5
S.D 0(R1),F4 S.D -8(R1),F8 ADD.D F28,F26,F2 6
S.D -16(R1),F12 S.D -24(R1),F16 7
S.D -32(R1),F20 S.D -40(R1),F24 SUBI R1,R1,#48 8
S.D -0(R1),F28 BNEZ R1,LOOP 9
Assumptions: L.D takes 2 cycles, ADD.D takes 3
Unrolled 7 times to avoid delays
7 results in 9 clocks, or 1.3 clocks per iteration
Need more registers in VLIW

## Slide 13: Limits to Multi-Issue Machines
Inherent limitations of ILP
  1 branch in 5 instructions: How to keep a 5-way VLIW busy?
  Latencies of units: many operations must be scheduled
  #independent instr. needed: Pipeline Depth  Number of FU
    ~15-20 independent instructions!
Difficulties in building the underlying hardware
  Large increase in bandwidth of memory and register-file
Limitations specific to either SS or VLIW implementation
  Decode issue in SS
  VLIW code size: unroll loops + wasted fields in VLIW
  VLIW lock step  1 hazard & all instructions stall
  VLIW & binary compatibility is practical weakness

## Slide 14: Hardware Support for More ILP
Avoid branch prediction by turning branches into conditionally executed instructions:
    if (x) then A = B op C else NOP
  If false, then do nothing at all
    neither store result nor cause exception
  Expanded ISA of Alpha, MIPS, PowerPC, SPARC have conditional move (CMOV)
Drawbacks to conditional instructions
  Still takes a clock even if “annulled”
  Stall if condition evaluated late
  Complex conditions reduce effectiveness; condition becomes known late in pipeline

## Slide 15: Hardware Support for More ILP
Speculation: allow an instruction to issue that is dependent on branch predicted to be taken without any consequences (including exceptions) if branch is not actually taken
  Hardware needs to provide an “undo” operation = squash
Often try to combine with dynamic scheduling
Tomasulo: compute speculatively, “commit” later
  When instruction no longer speculative, write results (instruction commit)
  execute out-of-order but commit in order
  Example: PowerPC 620, MIPS R10000, Intel P6, AMD K5 …

## Slide 16: Hardware support for More ILP
Need HW buffer for results of uncommitted instructions: reorder buffer (ROB)
  Reorder buffer can be operand source
  Once instruction commits, result is found in register
  3 fields: instr. type, destination, value
  Use reorder buffer number instead of reservation station
  Instructions commit in order
  As a result, its easy to undo speculated instructions on mispredicted branches or on exceptions
Reorder
Buffer
FP Regs
Instr
Queue
FP Adder
FP Mult
Res Stations
Res Stations

## Slide 17: Four Steps of Speculative Tomasulo Algorithm
1. Issue—get instruction from FP Op Queue
  If reservation station and reorder buffer slot free, issue instruction & send operands & reorder buffer no. for destination; each RS now also has a field for ROB#.
2. Execution—operate on operands (EX)
  When both operands ready then execute; if not ready, watch CDB for result; when both in reservation station, execute
3. Write result—finish execution (WB)
  Write on Common Data Bus to all awaiting RS’s & ROB; mark RS available
4. Commit—update register with reorder result
  When instruction at head of reorder buffer & result present, update register with result (or store to memory) and remove instruction from reorder buffer

## Slide 18: Result Shift Register and Reorder Buffer
General solution to three problems
  Precise exceptions
  Speculative execution
  Register renaming
Solution in three steps
  In-order initiation, out-of-order termination (using RSRa)
  In-order initiation, in-order termination (using RSRb)
  In-order initiation, in-order termination, with renaming (using ROB)
Architectural model
  Essentially MIPS FP pipeline
  FP add/sub takes 2 clock cycles, multiplication 5, division 10
  Memory accesses take 1 clock cycle
  Integer instructions take 1 clock cycle
  1 branch delay slot, delayed branches

## Slide 19: Step I: I-O Initiation, O-O Termination (RSRa)
LOOP:
LD F6, 32(R2)
LD F2, 48(R3)
MULTD F0, F2, F4
ADDI R2, R2, 8
ADDI R3, R3, 8
SUBD F8, F6, F2
DIVD F10, F10, F0
ADDD F6, F8, F6
BLEZ R4, LOOP
ADDI R4, R4, 1

## Slide 20: Step II: I-O Initiation, I-O Termination (RSRb)

## Slide 21: Step III: Use Re-order Buffer (ROB)
Combine benefits of early issue and in-order update of state
Obtained from RSRa by adding a renaming mechanism to it
Add a FIFO to RSRa (implement as circular buffer)
When RSRa allows issuing of new instruction
  Enter instruction at tail of circular buffer
  Buffer entry has multiple fields
    [Result; Valid Bit; Destination Register Name; PC value; Exceptions]
Termination happens when result is produced, broadcast on CDB, written into circular buffer (replace M with T)
  Written ROB entry can serve as source of operands from now on
Commit happens when value is moved from circular buffer to register (replace W with C)
  Happens when instruction reaches head of circular buffer and has completed execution with no exceptions

## Slide 22: ROB: I-O Initiation, I-O Termination
LOOP:
LD F6, 32(R2)
LD F2, 48(R3)
MULTD F0, F2, F4
ADDI R2, R2, 8
ADDI R3, R3, 8
SUBD F8, F6, F2
DIVD F10, F10, F0
ADDD F6, F8, F6
BLEZ R4, LOOP
ADDI R4, R4, 1

## Slide 23: States of Circular Reorder Buffer
LOOP:
LD F6, 32(R2)
LD F2, 48(R3)
MULTD F0, F2, F4
ADDI R2, R2, 8
ADDI R3, R3, 8
SUBD F8, F6, F2
DIVD F10, F10, F0
ADDD F6, F8, F6
BLEZ R4, LOOP
ADDI R4, R4, 1
Entry in yellow is at head of buffer
Entry in green is tail of buffer,
i.e., next instruction goes here
Greyed instructions have committed

## Slide 24: Tomasulo With Reorder buffer:
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
LD F0,10(R2)
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 25: Tomasulo With Reorder buffer:
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F10
F0
ADDD F10,F4,F0
LD F0,10(R2)
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 26: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 27: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 28: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 29: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F0
ADDD F0,F4,F6
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 30: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
6 ADDD ROB5, R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
ROB5
ST F4,0(R3)
ADDD F0,F4,F6
N
N
F4
LD F4,0(R3)
N
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
Dest
Reorder Buffer
Registers
1 10+R2
5 0+R3
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 31: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[30]
ST 0(R3),F4
ADDD F0,F4,F6
Y
N
F4
M[30]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
2 ADDD R(F4),ROB1
6 ADDD M[30],R(F6)
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 32: Tomasulo With Reorder buffer:
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
--
F0
M[30]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[30]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 33: Tomasulo With Reorder buffer:
--
F0
M[30]
<val2>
ST 0(R3),F4
ADDD F0,F4,F6
Y
Ex
F4
M[30]
LD F4,0(R3)
Y
--
BNE F2,<…>
N
3 DIVD ROB2,R(F6)
2 ADDD R(F4),ROB1
To
Memory
FP adders
FP multipliers
Reservation
Stations
FP Op
Queue
ROB7
ROB6
ROB5
ROB4
ROB3
ROB2
ROB1
F2
F10
F0
DIVD F2,F10,F6
ADDD F10,F4,F0
LD F0,10(R2)
N
N
N
Done?
Dest
Dest
Oldest
Newest
from
Memory
1 10+R2
Dest
Reorder Buffer
Registers
What about memory
hazards???
Notes: Resolve RAW memory conflict? (address in memory buffers)
Integer unit executes in parallel

## Slide 34: Avoiding Memory Hazards
WAW and WAR hazards through memory are eliminated because updating of memory occurs in order, when a store is at head of the ROB
  no earlier loads or stores can still be pending
RAW hazards through memory are maintained by two restrictions:
  not allowing a load to initiate the second step of its execution if any active ROB entry occupied by a store has a Destination field that matches the value of the A field of the load, and
  maintaining the program order for the computation of an effective address of a load with respect to all earlier stores.
So, load that accesses a memory location written to by an earlier store can’t perform the memory access until the store has written the data

## Slide 35: Complexity of ROB
Assume dual-issue superscalar
  Load/Store machine with three-operand instructions
  64 registers
  16-entry circular buffer
Hardware support needed for ROB
  For each buffer entry
    One write port
    Four read ports (two source operands of two instructions)
    Four 6-bit comparators for associative lookup
  For each read port
    16-way “priority” encoder with wrap-around (to get latest value)
Limited capacity of ROB is a structural hazard
Repeated writes to same register actually happen
  This is not the case in “classical” Tomasulo