## Slide 1
The Cray 1, a vector supercomputer. The first model ran at 80MHz but could retire 2 instructions/cycle for a peak of 160 MIPS. However, it could reach 250 MFLOPS using vectors.

## Slide 2: COMP 740: Computer Architecture and Implementation
Montek Singh
Nov 16, 2016
Topic: Vector Processing

## Slide 3: Traditional Supercomputer Applications
Typical application areas
  Military research (nuclear weapons, cryptography)
  Scientific research
  Weather forecasting
  Oil exploration
  Industrial design (car crash simulation)
All involve huge computations on large data sets
In 70s-80s, Supercomputer  Vector Machine

## Slide 4: Vector Supercomputers
Epitomized by Cray-1, 1976:
  Scalar Unit + Vector Extensions
    Load/Store Architecture
    Vector Registers
    Vector Instructions
    Hardwired Control
    Highly Pipelined Functional Units
    Interleaved Memory System
    No Data Caches
    No Virtual Memory

## Slide 5: Cray-1 (1976)

## Slide 6: Vector Programming Model
+
+
+
+
+
+
[0]
[1]
[VLR-1]
Vector Arithmetic Instructions
ADDV v3, v1, v2
v3
v2
v1
Scalar Registers
r0
r15
Vector Registers
v0
v15
[0]
[1]
[2]
[VLRMAX-1]
VLR
Vector Length Register
v1
Vector Load/Store instr
LVWS v1, (r1, r2)
LV v1, r1
Base, r1
Stride, r2
Memory
Vector Register

## Slide 7: Vector Code Example
# Scalar Code
LI R4, 64
loop:
L.D F0, 0(R1)
L.D F2, 0(R2)
ADD.D F4, F2, F0
S.D F4, 0(R3)
DADDIU R1, 8
DADDIU R2, 8
DADDIU R3, 8
DSUBIU R4, 1
BNEZ R4, loop
# Vector Code
LI VLR, 64
LV V1, R1
LV V2, R2
ADDV.D V3, V1, V2
SV V3, R3
# C code
for (i=0; i<64; i++)
C[i] = A[i] + B[i];

## Slide 8: Vector Arithmetic Execution
Use deep pipeline (=> fast clock) to execute element operations
Simplifies control of deep pipeline because elements in vector are independent (=> no hazards!)
V1
V2
V3
V3 <- v1 * v2
Six stage multiply pipeline

## Slide 9: Vector Instruction Execution
ADDV C,A,B
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
Execution using one pipelined functional unit
C[4]
C[8]
C[0]
A[12]
B[12]
A[16]
B[16]
A[20]
B[20]
A[24]
B[24]
C[5]
C[9]
C[1]
A[13]
B[13]
A[17]
B[17]
A[21]
B[21]
A[25]
B[25]
C[6]
C[10]
C[2]
A[14]
B[14]
A[18]
B[18]
A[22]
B[22]
A[26]
B[26]
C[7]
C[11]
C[3]
A[15]
B[15]
A[19]
B[19]
A[23]
B[23]
A[27]
B[27]
Execution using four pipelined functional units

## Slide 10: Vector Unit Structure
Lane
Functional Unit (e.g., adders)
Vector
Registers
Vector load-store unit (Memory Subsystem)
Elements 0, 4, 8, …
Elements 1, 5, 9, …
Elements 2, 6, 10, …
Elements 3, 7, 11, …
Functional Unit (e.g., multipliers)

## Slide 11: Vector Memory-Memory vs. Vector Register
Vector memory-memory instructions hold all vector operands in main memory
The first vector machines, CDC Star-100 (‘73) and TI ASC (‘71), were memory-memory machines
Cray-1 (’76) was first vector register machine
for (i=0; i<N; i++)
{
C[i] = A[i] + B[i];
D[i] = A[i] - B[i];
}
Example Source Code
ADDV C, A, B
SUBV D, A, B
Vector Memory-Memory Code
LV V1, A
LV V2, B
ADDV V3, V1, V2
SV V3, C
SUBV V4, V1, V2
SV V4, D
Vector Register Code

## Slide 12: Vector Memory-Memory vs. Vector Register
Vector memory-memory architectures (VMMA) require greater main memory bandwidth, why?
  All operands must be read in and out of memory
VMMAs make if difficult to overlap execution of multiple vector operations, why?
  Must check dependencies on memory addresses
  Apart from CDC follow-ons (Cyber-205, ETA-10) all major vector machines since Cray-1 have had vector register architectures
  (we ignore vector memory-memory from now on)

## Slide 13: Automatic Code Vectorization
for (i=0; i < N; i++)
C[i] = A[i] + B[i];
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Scalar Sequential Code
Vectorization is a massive compile-time reordering of operation sequencing
 requires extensive loop dependence analysis
Vector Instruction
load
load
add
store
load
load
add
store
Iter. 1
Iter. 2
Vectorized Code
Time

## Slide 14: Vector Strip Mining
Problem: Vector registers have finite length
Solution: Break loops into pieces that fit into vector registers, “Strip mining”
ANDI R1, N, 63 # N mod 64
MTC1 VLR, R1 # Do remainder
loop:
LV V1, RA
DSLL R2, R1, 3 # Multiply by 8
DADDU RA, RA, R2 # Bump pointer
LV V2, RB
DADDU RB, RB, R2
ADDV.D V3, V1, V2
SV V3, RC
DADDU RC, RC, R2
DSUBU N, N, R1 # Subtract elements
LI R1, 64
MTC1 VLR, R1 # Reset full length
BGTZ N, loop # Any more to do?
for (i=0; i<N; i++)
C[i] = A[i]+B[i];
+
+
+
A
B
C
64 elements
Remainder

## Slide 15: Vector Instruction Parallelism
load
Can overlap execution of multiple vector instructions
  example machine has 32 elements per vector register and 8 lanes
load
mul
mul
add
add
Load Unit
Multiply Unit
Add Unit
time
Instruction issue
Complete 24 operations/cycle while issuing 1 short instruction/cycle

## Slide 16: Vector Chaining
Vector version of register bypassing
  introduced with Cray-1
Memory
V1
Load Unit
Mult.
V2
V3
Chain
Add
V4
V5
Chain
LV v1
MULV v3,v1,v2
ADDV v5, v3, v4

## Slide 17: Vector Chaining Advantage
With chaining, can start dependent instruction as soon as first result appears
Load
Mul
Add
Load
Mul
Add
Time
Without chaining, must wait for last element of result to be written before starting dependent instruction

## Slide 18: Memory operations
32
Load/store operations move groups of data between registers and memory
Types of addressing
  Unit stride
    Contiguous block of information in memory
    Fastest: always possible to optimize this
      LV v1, r1
  Non-unit (constant) stride
    Harder to optimize memory system for all possible strides
    Prime number of data banks makes it easier to support different strides at full bandwidth
      LVWS v1, (r1, r2)

## Slide 19: Vector Memory System
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F
+
Base
Stride
Vector Registers
Memory Banks
Address Generator
Cray-1, 16 banks, 4 cycle bank busy time, 12 cycle latency
  Bank busy time: Cycles between accesses to same bank

## Slide 20: Interleaved Memory Layout
Great for unit stride:
  Contiguous elements in different DRAMs
  Startup time for vector operation is latency of single read
What about non-unit stride?
  Above good for strides that are relatively prime to 16
  Bad for: 2, 4, 8
  Better: prime number of banks…!

## Slide 21: Vector Scatter/Gather
Want to vectorize loops with indirect accesses:
  for (i=0; i<N; i++)
  A[i] = B[i] + C[D[i]]
Indexed load instruction (Gather)
  LV vD, rD # Load indices in D vector
  LVI vC, rC, vD # Load indirect from rC base
  LV vB, rB # Load B vector
  ADDV.D vA, vB, vC # Do add
  SV vA, rA # Store result

## Slide 22: Vector Conditional Execution
Problem: Want to vectorize loops with conditional code:
      for (i=0; i<N; i++)
      if (A[i]>0) then
      A[i] = B[i];
Solution: Add vector mask (or flag) registers
  vector version of predicate registers, 1 bit per element
…and maskable vector instructions
  vector operation becomes NOP at elements where mask bit is clear

## Slide 23: Masked Vector Instructions
C[4]
C[5]
C[1]
Write data port
A[7]
B[7]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
Density-Time Implementation
  scan mask vector and only execute elements with non-zero masks
C[1]
C[2]
C[0]
A[3]
B[3]
A[4]
B[4]
A[5]
B[5]
A[6]
B[6]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
Write data port
Write Enable
A[7]
B[7]
M[7]=1
Simple Implementation
  execute all N operations, turn off result writeback according to mask

## Slide 24: Compress/Expand Operations
Compress packs non-masked elements from one vector register contiguously at start of destination vector register
  population count of mask vector gives packed vector length
Expand performs inverse operation
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
A[3]
A[4]
A[5]
A[6]
A[7]
A[0]
A[1]
A[2]
M[3]=0
M[4]=1
M[5]=1
M[6]=0
M[2]=0
M[1]=1
M[0]=0
M[7]=1
B[3]
A[4]
A[5]
B[6]
A[7]
B[0]
A[1]
B[2]
Expand
A[7]
A[1]
A[4]
A[5]
Compress
A[7]
A[1]
A[4]
A[5]

## Slide 25: Vector Reductions
Problem: Loop-carried dependence on reduction variables
  sum = 0;
  for (i=0; i<N; i++)
  sum += A[i]; # Loop-carried dependence on sum
Solution: Re-associate operations if possible, use binary tree to perform reduction
  # Rearrange as:
  sum[0:VL-1] = 0 # Vector of VL partial sums
  for(i=0; i<N; i+=VL) # Stripmine VL-sized chunks
  sum[0:VL-1] += A[i:i+VL-1]; # Vector sum
  # Now have VL partial sums in one vector register
  do {
  VL = VL/2; # Halve vector length
  sum[0:VL-1] += sum[VL:2*VL-1] # Halve no. of partials
  } while (VL>1)

## Slide 26: Vector Execution Time
Time = f(vector length, data dependencies, struct. hazards)
Initiation rate: rate that FU consumes vector elements (= number of lanes; usually 1 or 2 on Cray T-90)
Convoy: set of vector instructions that can begin execution in same clock (no struct. or data hazards)
Chime: approx. time for a vector operation
m convoys take m chimes; if each vector length is n, then they take approx. m x n clock cycles (ignores overhead; good approximization for long vectors)
4 convoys, 1 lane, VL=64
=> 4 x 64 = 256 clocks
(or 4 clocks per result)
1: LV V1,Rx ;load vector X
2: MULV V2,F0,V1 ;vector-scalar mult.
LV V3,Ry ;load vector Y
3: ADDV V4,V2,V3 ;add
4: SV Ry,V4 ;store the result

## Slide 27: Older Vector Machines
Machine Year Clock Regs Elements FUs
Cray 1 1976 80 MHz 8 64 6
Cray XMP 1983 120 MHz 8 64 8
Cray YMP 1988 166 MHz 8 64 8
Cray C-90 1991 240 MHz 8 128 8
Cray T-90 1996 455 MHz 8 128 8
Convex C-1 1984 10 MHz 8 128 4
Convex C-4 1994 133 MHz 16 128 3
Fuj. VP200 1982 133 MHz 8-256 32-1024 3
Fuj. VP300 1996 100 MHz 8-256 32-1024 3
NEC SX/2 1984 160 MHz 8+8K 256+var 16
NEC SX/3 1995 400 MHz 8+8K 256+var 16
Notes: Cray 1; fastest scalar computer + 1st commercially successful vector computer, offered another 10X
6600 1st scoreboard
Cray XMP: 3 LSUs, Multiprocessor 4 way (not by Cray)
=> YMP, C-90, T-90; 2X processors, 1.5X clock
Cray 2 went to DRAM to get more memory, not so great
Like parallel teams as Intel (486, PPro, Pentium, next one)
Japan
Fujitsu, vary number of registers elements (8x1024 or 32x256)
NEC, 8x256 + 8K of varying elements

## Slide 28: Newer Vector Computers
Cray X1 & X1E
  MIPS like ISA + Vector in CMOS
NEC Earth Simulator
  Fastest computer in world for 3 years; 40 TFLOPS
  640 CMOS vector nodes

## Slide 29: Key Architectural Features of X1
New vector instruction set architecture (ISA)
  Much larger register set (32x64 vector, 64+64 scalar)
  64- and 32-bit memory and IEEE arithmetic
  Based on 25 years of experience compiling with Cray1 ISA
Decoupled Execution
  Scalar unit runs ahead of vector unit, doing addressing and control
  Hardware dynamically unrolls loops, and issues multiple loops concurrently
  Special sync operations keep pipeline full, even across barriers
   Allows the processor to perform well on short nested loops
Scalable, distributed shared memory (DSM) architecture
  Memory hierarchy: caches, local memory, remote memory
  Low latency, load/store access to entire machine (tens of TBs)
  Processors support 1000’s of outstanding refs with flexible addressing
  Very high bandwidth network
  Coherence protocol, addressing and synchronization optimized for DM

## Slide 30: Cray X1E Mid-life Enhancement
Technology refresh of the X1 (0.13m)
  ~50% faster processors
  Scalar performance enhancements
  Doubling processor density
  Modest increase in memory system bandwidth
  Same interconnect and I/O
Machine upgradeable
  Can replace Cray X1 nodes with X1E nodes

## Slide 31: Earth Simulator
Processor Nodes (PN) Total number of processor nodes is 640. Each processor node consists of eight vector processors of 8 GFLOPS and 16GB shared memories. Therefore, total numbers of processors is 5,120 and total peak performance and main memory of the system are 40 TFLOPS and 10 TB, respectively. Two nodes are installed into one cabinet, size is 40”x56”x80”. 16 nodes are in a cluster. Power consumption per cabinet is approximately 20 KW.
2) Interconnection Network (IN): Each node is coupled together with more than 83,000 copper cables via single-stage crossbar switches of 16GB/s x2 (Load + Store). The total length of the cables is approximately 1,800 miles.
3) Hard Disk. Raid disks are used for the system. The capacities are 450 TB for the systems operations and 250 TB for users.
4) Mass Storage system: 12 Automatic Cartridge Systems (STK PowderHorn9310); total storage capacity is approximately 1.6 PB.
From Horst D. Simon, NERSC/LBNL, May 15, 2002, “ESS Rapid Response Meeting”
A general-purpose supercomputer:

## Slide 32: Earth Simulator

## Slide 33: Earth Simulator Building

## Slide 34: ESS – complete system installed 4/1/2002

## Slide 35: Multimedia Extensions
Very short vectors added to existing ISAs for micros
Usually 64-bit registers split into 2x32b or 4x16b or 8x8b
Newer designs have 128-bit registers (Altivec, SSE2)
Limited instruction set:
  no vector length control
  no strided load/store or scatter/gather
  unit-stride loads must be aligned to 64/128-bit boundary
Limited vector register length:
  requires superscalar dispatch to keep multiply/add/load units busy
  loop unrolling to hide latencies increases register pressure
Trend towards fuller vector support in microprocessors

## Slide 36: Vector Instruction Set Advantages
Compact
  one short instruction encodes N operations
Expressive, tells hardware that these N operations:
  are independent
  use the same functional unit
  access disjoint registers
  access registers in the same pattern as previous instructions
  access a contiguous block of memory (unit-stride load/store)
  access memory in a known pattern (strided load/store)
Scalable
  can run same object code on more parallel pipelines or lanes

## Slide 37: Operation & Instruction Count: RISC v. Vector Processor
Spec92fp Operations (Millions) Instructions (Millions)
Program RISC Vector R/V RISC Vector R/V
swim256 115 95 1.1x 115 0.8 142x
hydro2d 58 40 1.4x 58 0.8 71x
nasa7 69 41 1.7x 69 2.2 31x
su2cor 51 35 1.4x 51 1.8 29x
tomcatv 15 10 1.4x 15 1.3 11x
wave5 27 25 1.1x 27 7.2 4x
mdljdp2 32 52 0.6x 32 15.8 2x
Vector reduces ops by 1.2X, instructions by 20X
(from F. Quintana, U. Barcelona.)

## Slide 38: Vectors Lower Power
Vector
One inst fetch, decode, dispatch per vector
Structured register accesses
Smaller code for high performance, less power in instruction cache misses
Bypass cache
One TLB lookup per group of loads or stores
Move only necessary data across chip boundary
Single-issue Scalar
One instruction fetch, decode, dispatch per operation
Arbitrary register accesses, adds area and power
Loop unrolling and software pipelining for high performance increases instruction cache footprint
All data passes through cache; waste power if no temporal locality
One TLB lookup per load or store
Off-chip access in whole cache lines
Notes: 41

## Slide 39: Superscalar: Worse Energy Efficiency
Vector
Control logic grows linearly with issue width
Vector unit switches off when not in use
Vector instructions expose parallelism without speculation
Software control of speculation when desired:
  Whether to use vector mask or compress/expand for conditionals
Superscalar
Control logic grows quadratically with issue width
Control logic consumes energy regardless of available parallelism
Speculation to increase visible parallelism wastes energy
Notes: 42

## Slide 40: Vector Applications
Limited to scientific computing? No!
  Multimedia Processing (compress., graphics, audio synth, image proc.)
  Standard benchmark kernels (Matrix Multiply, FFT, Convolution, Sort)
  Lossy Compression (JPEG, MPEG video and audio)
  Lossless Compression (Zero removal, RLE, Differencing, LZW)
  Cryptography (RSA, DES/IDEA, SHA/MD5)
  Speech and handwriting recognition
  Operating systems/Networking (memcpy, memset, parity, checksum)
  Databases (hash/join, data mining, image/video serving)
  Language run-time support (stdlib, garbage collection)
  even SPECint95
Notes: 43

## Slide 41: Vector Summary
Vector is alternative model for exploiting ILP
If code is vectorizable, then simpler hardware, more energy efficient, and better real-time model than Out-of-order machines
Design issues include number of lanes, number of functional units, number of vector registers, length of vector registers, exception handling, conditional operations
Fundamental design issue is memory bandwidth
Will multimedia popularity revive vector architectures?