## Slide 1: Memories and State Machines
Don Porter
Lecture 13

## Slide 2: Topics
Memory Arrays
Transparent Latches
Edge-Triggered Registers
Finite State Machines

## Slide 3: Read-Only Memory = a Lookup Table
A multiplexer can implement a lookup table:
  for an N-input function we need a 2N input multiplexer
  simply select one row out of 2N
  2N values go into the mux, only one comes out
  N-bit select input is now the “address” of data being accessed
Limitations:
  mux can get really big: 10-bit address  1024 rows!
  read-only; we also would like to write!
MUX
Logic
A
B
Fn(A,B)
Read-Only Memory (ROM)
Notes: For N-input function, need
  N select inputs to MUX
  2**N data inputs to MUX (LOTSA pins!)
Practical TABLE LOOKUP needs more efficient
use of space...
2n
2n
2
1024-input MUX???

## Slide 4: A Mux’s Guts: Decoder + Selector
Hmmm, by sharing the decoder part of the logic MUXs could be adapted to make lookup tables with any number of outputs
I
0
0
I
0
1
I
1
0
I
1
1
A
B
A
B
A
B
A
B
Y
Decoder
Selector
Multiplexers can be partitioned into two sections.
A DECODER that identifies the desired input,and
a SELECTOR that enables that input onto the output.
A decoder generates all possible product terms for a set of inputs
0
1
2
3
Notes: ... THIS one AIN’T!

## Slide 5: Decoder
k
D1
D2
DN
DECODER:
  k SELECT inputs,
  N = 2k DATA OUTPUTs.
Selected Dj HIGH; all others LOW.
NOW, we are well on our way to building a general purpose table-lookup device.
We can build a 2-dimensional ARRAY of decoders and selectors as follows ...
Notes: DECODER -- sorta inverse MUX.
  BINARY number as input
  UNARY (decoded) output.

## Slide 6: Shared Decoding Logic
We can build a general purpose “table-lookup” device called a Read-Only Memory (ROM), from which we can implement any truth table and, thus, any combinational device

## Slide 7: Logic According to ROMs
Different ROM implementation technologies
  Mask (old)  ROM
    read-only memory
  Fuses (old)  PROM
    programmable read-only memory
  Erasable  EPROM
    erasable programmable read-only memory
  Electrically erasable  EEPROM
    electrically-erasable programmable read-only memory
    today called FLASH! Used everywhere!
Model: LOOK UP value of function in truth table...
  Inputs: “ADDRESS” of a truth table entry
  ROM SIZE = # truth table entries...
    ... for an N-input boolean function, size = ____________
2N x #outputs
Notes: 2-D: 2x/dimension
NOT OPTIMAL -- Optimized for WORST case
(NO structure in TT entries!)
ADVANTAGE: Flexibility.
CHANGE function with little change in HW.

## Slide 8: Read-Write Memories (RAM)
Read-Write often called random-access memories (RAM)
Dynamic RAM uses analog storage:
  encode information using voltages
  from physics: we can “store” a voltage as “charge” on a capacitor
  Pros:
    compact!
  Cons:
    it leaks! -> refresh
    complex interface
    reading a bit, destroys it
      (you have to rewrite the value after each read)
    it’s NOT a digital circuit
To write:
Drive bit line, turn on access transistor, force storage cap to new voltage To read: precharge bit line, turn on access trans.,
detect (small) change in bit line voltage
bit line
N-transistor
serves
as an access switch
VREF
word
line
  This storage circuit is the basis for commodity DRAMs

## Slide 9: Static RAM: A “Digital” Storage Element
Y
S
B
It’s also easy to build a DIGITAL storage element (called a latch) using a MUX and FEEDBACK:
0
1
G
0
0
1
1
D
--
--
0
1
QIN
0
1
--
--
QOUT
0
1
0
1
Q follows D
Q stable
“state” signal
appears as both
input and output
A
D
G
Q
Here’s a feedback path, so it’s no longer a combinational circuit.

## Slide 10: Static D Latch
G
D
Q
D
G
Q stable
Q follows D
Positive latch
Q
“static” means latch will hold data (i.e., value of Q) while G is inactive, however long that may be.
G
D
Q
Negative latch
Q
G
D
1
0

## Slide 11: Latch Timing
Circuits with memory must follow some rules
  Guarantee that inputs to sequential devices are valid and stable during periods when they may influence state changes
    This is assured with additional timing specifications
G
D
>tPULSE
tPULSE (minimum pulse width): guarantee G is active for long enough for latch to capture data
>tSETUP
tSETUP (setup time): guarantee that D value has propagated through feedback path before latch becomes opaque
>tHOLD
tHOLD (hold time): guarantee latch is opaque and Q is stable before allowing D to change again

## Slide 12: Effects of transparency
Toll Booth Analogy

## Slide 13: Flakey Control Systems
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!

## Slide 14: Flakey Control Systems
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!

## Slide 15: Flakey Control Systems
WARNING:
DON’T try this
At home!
Here’s a strategy for saving 2 bucks the next time you find yourself at a toll booth!

## Slide 16: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 17: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 18: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 19: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 20: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 21: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 22: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 23: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 24: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 25: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 26: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 27: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 28: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 29: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 30: Escapement Strategy
The Solution:
Add two gates and only open one at a time.

## Slide 31: Escapement Strategy
Key Idea: At no time is there an open path through both gates…
The Solution:
Add two gates and only open one at a time.

## Slide 32: D Flip-Flop (Edge-Triggered Flip-Flop)
Logical “escapement”:
  Double-gated toll booth built using logic gates
Observations:
  only one latch “transparent” at any time:
    L1 opaque when L2 is transparent (CLK is high)
    L2 opaque when L1 is transparent (CLK is low)
    no combinational path all the way through flip flop
  Q only changes shortly after 0 1 transition of CLK, so flip flop appears to be “triggered” by rising edge of CLK
G
D
Q
G
D
Q
D
Q
D
CLK
Q
D
CLK
Q
L1
L2
Transitions mark instants, not intervals

## Slide 33: D Flip-Flop: Operation
Edge-triggered
  when CLK goes from 0 to 1
    output Q is updated once to the input D value
  all other times, output is held
Why?
  L1 is transparent when CLK=0
    the last value of D that goes through to N1 is when CLK goes to 1
  L2 is transparent when CLK=1
    the value that goes through is N1
    i.e., last value of D just before CLK goes to 1
G
D
Q
G
D
Q
D
Q
D
CLK
Q
D
CLK
Q
L1
L2

## Slide 34: Flip Flop Waveforms
G
D
Q
G
D
Q
D
Q
D
CLK
Q
D
CLK
Q
L1
L2
D
CLK
Q
L1 closed
L2 open
L2 closed
L1 open

## Slide 35: Flip Flop Timing
CLK
D
Q
D
Q
D
CLK
Q
<tPD
tPD: maximum propagation delay, CLK Q
>tSETUP
tSETUP: setup time
  guarantee that D has propagated through feedback path before L1 closes
>tHOLD
tHOLD: hold time
  guarantee L1 is closed and data is stable before allowing D to change

## Slide 36: Synchronous Systems
Designing digital systems using a clock

## Slide 37: Synchronous Systems
Flipflop
Combinational
logic
Flipflop
leading
edge
trailing
edge
On the leading edge of the clock, the input of a flipflop is transferred to the output and held.
We must be sure the output of the combinational logic has settled before the next leading clock edge.
Clock
data
Clock period must be “long enough”
Clock Period >= tFF + tlogic + tsetup

## Slide 38: Finite State Machines
What is a State Machine?
  Remember automata?
  It is defined by the following:
    Set of STATES
    Set of INPUTS
    Set of OUTPUTS
    A mapping from (STATES, INPUTS) to …
    … the next STATE and an OUTPUT
  STATE represents memory!

## Slide 39: Implementing an FSM
Use flipflops to represent state (i.e., memory)
Use combinational logic to compute:
  output as a function of inputs + state
  next state as a function of inputs + state
State (flipflops)
Function
(comb. logic)
Inputs
Outputs
Clock

## Slide 40: Example: Traffic Light Controller
4 states
  each corresponding to a circle
  represent states using 2 bits
    00, 01, 10, 11
4 bits of output
  2 bits for east/west light
  2 bits for north/south light
    Red (00)
    Yellow (01)
    Green (10)
G E/W
R N/S
Y E/W
R N/S
R E/W
G N/S
R E/W
Y N/S

## Slide 41: Example: Traffic Light Controller
4 states
    00, 01, 10, 11
    need 2 flipflops to represent state
4 bits of output
    R (00), Y (01), G (10)
Truth table:
    this defines the combinational logic part of the FSM
G E/W
R N/S
Y E/W
R N/S
R E/W
G N/S
R E/W
Y N/S
Input (State) | Output | Next State
00 | 10 00 | 01
01 | 01 00 | 10
10 | 00 10 | 11
11 | 00 01 | 00

## Slide 42: Summary
Regular Arrays can be used to implement arbitrary logic functions
Memories
  ROMs are HARDWIRED memories
  RAMs include storage elements that are read-write
    dynamic memory: compact, only reliable short-term
    static memory: controlled use of positive feedback
For static storage:
  Level-sensitive D-latches; edge-triggered flipflops
  Timing issues: setup and hold times
Finite State Machines:
  Implement using flipflops for memory, and combinational logic to compute output, next state