## Slide 1: Locking
Don Porter
Portions courtesy Emmett Witchel

## Slide 2: Too Much Milk: Lessons
Software solution (Peterson’s algorithm) works, but it is unsatisfactory
  Solution is complicated; proving correctness is tricky even for the simple example
  While thread is waiting, it is consuming CPU time
  Asymmetric solution exists for 2 processes.
How can we do better?
  Use hardware features to eliminate busy waiting
  Define higher-level programming abstractions to simplify concurrent programming

## Slide 3: Concurrency Quiz
If two threads execute this program concurrently, how many different final values of X are there?
Initially, X == 0.
void increment() {
int temp = X;
temp = temp + 1;
X = temp;
}
void increment() {
int temp = X;
temp = temp + 1;
X = temp;
}
Thread 1
Thread 2
Answer:
0
1
2
More than 2
Notes: Answer: C I think

## Slide 4: Schedules and Interleavings
Model of concurrent execution
Interleave statements from each thread into a single thread
If any interleaving yields incorrect results, some synchronization is needed
tmp1 = X;
tmp1 = tmp1 + 1;
X = tmp1;
tmp2 = X;
tmp2 = tmp2 + 1;
X = tmp2;
Thread 1
Thread 2
tmp1 = X;
tmp2 = X;
tmp2 = tmp2 + 1;
tmp1 = tmp1 + 1;
X = tmp1;
X = tmp2;
If X==0 initially, X == 1 at the end. WRONG result!

## Slide 5: Locks fix this with Mutual Exclusion
Key abstraction: mutual exclusion while lock is held
Goal: ”Protect” unsafe code from dangerous interleavings
  At some loss of concurrency
void increment() {
pthread_mutex_lock(&lock);
int temp = X;
temp = temp + 1;
X = temp;
pthread_mutex_unlock(&lock);
}

## Slide 6: Introducing Locks
Locks – implement mutual exclusion
  Two methods
    pthread_mutex_lock(lock) – wait until lock is free, then grab it
    pthread_mutex_unlock(lock) – release the lock, waking up a waiter, if any
With locks, too much milk problem is very easy!
  Check and update happen as one unit (exclusive access)
Lock.Acquire();
if (noMilk) {
buy milk;
}
Lock.Release();
Lock.Acquire();
x++;
Lock.Release();
  How can we implement locks?

## Slide 7: Performance: Between rock and hard place
We need threads for concurrent performance
We can’t safely execute all code concurrently
  Locks ensure that ”delicate” code does not interleave with other code that could interleave unsafely
It is safe to execute everything in one big lock
  But worse performance than a single thread
  No concurrency + overheads
Goal: get just enough mutual exclusion for safety, but no more than strictly necessary

## Slide 8: How do locks work?
Two key ingredients:
  A hardware-provided atomic instruction
    Determines who wins under contention
  A waiting strategy for the loser(s)

## Slide 9: Atomic instructions
A “normal” line of code (or CISC instruction) can span multiple memory operations
  Example: ‘a = b + c’ requires 2 loads and a store
  These loads and stores can interleave with other CPUs’ memory accesses
An atomic instruction guarantees that the entire operation is not interleaved with any other CPU
  x86: Certain instructions can have a ‘lock’ prefix
  Intuition: This CPU ‘locks’ all of memory
  Expensive! Not ever used automatically by a compiler; must be explicitly used by the programmer

## Slide 10: Atomic instruction examples
Atomic increment/decrement ( x++ or x--)
  int atomic_inc(int *var) {
  int rv = *var;
  *var++;
  return rv;
  }
  Used for reference counting,
  Returns old value that you specifically set
  If *var is 0, and 3 threads do an atomic_inc, one will get 1, one 2, and one 3
Atomic Test and Set:
  old = ts(&var)
  bool ts(int *) { bool ret = *int; *int = 1; return ret == 0;}
  Sets a value to 1 atomically; returns true if you were the thread that transitioned from 0 to 1
Compare and swap
  Common Syntax: cas(&var, old, new)
  {int rv = *var; if (*var == old) *var = new; return rv;}
  Used for many lock-free data structures
Notes: START HERE 18

## Slide 11: Atomic instructions + locks
Most lock implementations have some sort of counter
Say initialized to 1
To acquire the lock, use an atomic decrement
  Recall: atomic_dec returns the value your thread set
  If you set the value to 0, you win! Go ahead
  If you get < 0, you lose. Wait 
  Atomic decrement ensures that only one CPU will decrement the value to zero
To release, set the value back to 1

## Slide 12: Waiting strategies
Spinning: Just poll the atomic counter in a busy loop; when it becomes 1, try the atomic decrement again
Blocking: Create a kernel wait queue and go to sleep, yielding the CPU to more useful work
  Winner is responsible to wake up losers (in addition to setting lock variable to 1)
  Create a kernel wait queue – the same thing used to wait on I/O
    Reminder: Moving to a wait queue takes you out of the scheduler’s run queue

## Slide 13: Which strategy to use?
Main consideration: Expected time waiting for the lock vs. time to do 2 context switches
  If the lock will be held a long time (like while waiting for disk I/O), blocking makes sense
  If the lock is only held momentarily, spinning makes sense
Other, subtle considerations we will discuss later

## Slide 14: Reminder: Correctness Conditions
Safety
  Only one thread in the critical region
Liveness
  Some thread that enters the entry section eventually enters the critical region
  Even if other thread takes forever in non-critical region
Bounded waiting
  A thread that enters the entry section enters the critical section within some bounded number of operations.
Failure atomicity
  It is OK for a thread to die in the critical region
  Many techniques do not provide failure atomicity

## Slide 15: Example: Linux spinlock (simplified)
1: lock; decb slp->slock
jns 3f
2: pause
cmpb $0,slp->slock
jle 2b
jmp 1b
3:
// Locked decrement of lock var
// Jump if not set (result is zero) to 3
// Low power instruction, wakes on // coherence event
// Read the lock value, compare to zero
// If less than or equal (to zero), goto 2
// Else jump to 1 and try again
// We win the lock

## Slide 16: Rough C equivalent
while (0 != atomic_dec(&lock->counter)) {
do {
// Pause the CPU until some coherence // traffic (a prerequisite for the counter // changing) saving power
} while (lock->counter <= 0);
}
Notes: START HERE – set up the 2 loops question

## Slide 17: Why 2 loops?
Functionally, the outer loop is sufficient
Problem: Attempts to write this variable invalidate it in all other caches
  If many CPUs are waiting on this lock, the cache line will bounce between CPUs that are polling its value
    This is VERY expensive and slows down EVERYTHING on the system
  The inner loop read-shares this cache line, allowing all polling in parallel
This pattern called a Test&Test&Set lock (vs. Test&Set)

## Slide 18: Test & Set Lock
CPU 0
Cache
Memory Bus
0x1000
RAM
CPU 1
Cache
atomic_dec
  Cache Line “ping-pongs” back and forth
while (!atomic_dec(&lock->counter))
0x1000
CPU 2
// Has lock
atomic_dec
Write Back+Evict
Cache Line

## Slide 19: Test & Test & Set Lock
CPU 0
Cache
Memory Bus
0x1000
RAM
CPU 1
Cache
read
  Line shared in read mode until unlocked
while (lock->counter <= 0))
0x1000
CPU 2
// Has lock
read
Unlock by writing 1

## Slide 20: Why 2 loops?
Functionally, the outer loop is sufficient
Problem: Attempts to write this variable invalidate it in all other caches
  If many CPUs are waiting on this lock, the cache line will bounce between CPUs that are polling its value
    This is VERY expensive and slows down EVERYTHING on the system
  The inner loop read-shares this cache line, allowing all polling in parallel
This pattern called a Test&Test&Set lock (vs. Test&Set)

## Slide 21: Implementing Blocking Locks
pthread_mutex_lock() {
while (ts(lock) == 1)
; // spin
}
pthread_mutex_unlock() {
*lock := 0;
}
With busy-waiting
pthread_mutex_lock() {
while (ts(q_lock) == 1) {
Put TCB on wait queue for lock;
}
Without busy-waiting, use a queue
pthread_mutex_unlock() {
*q_lock = 0;
if (wait queue is not empty) {
Move 1 (or all?) waiting threads to ready queue;
}
  Must only one thread be awakened? Is this code fair?
Notes: START HERE 2020
Answer: no, other threads will spin in switch, could be improved

## Slide 22: Reader/writer locks
Simple optimization: If I am just reading, we can let other readers access the data at the same time
  Just no writers
Writers require mutual exclusion

## Slide 23: Best Practices for Lock Programming
When you enter a critical region, check what may have changed while you were spinning
  Did Jill get milk while I was waiting on the lock?
Always unlock any locks you acquire

## Slide 24: Implementing Locks: Summary
Locks are higher-level programming abstraction
  Mutual exclusion can be implemented using locks
Lock implementations have 2 key ingredients:
  Hardware instruction: atomic read-modify-write
  Blocking mechanism
    Busy waiting, or
      Cheap Busy waiting important
    Block on a scheduler queue in the OS
Locks are good for mutual exclusion but weak for coordination, e.g., producer/consumer patterns.

## Slide 25: Why locking is also hard (Preview)
Fine-grain locks
  Greater concurrency
  Greater code complexity
  Potential deadlocks
    Not composable
  Potential data races
    Which lock to lock?
// WITH FINE-GRAIN LOCKS
void move(T s, T d, Obj key){
pthread_mutex_lock(s);
pthread_mutex_lock(d);
tmp = s.remove(key);
d.insert(key, tmp);
pthread_mutex_unlock(d);
pthread_mutex_unlock(s);
}
DEADLOCK!
move(a, b, key1);
move(b, a, key2);
Thread 0
Thread 1
Coarse-grain locks
  Simple to develop
  Easy to avoid deadlock
  Few data races
  Limited concurrency