## Slide 1: COMP541 Combinational Logic - 4
Montek Singh
Sep {24, 26}, 2018

## Slide 2: Today’s Topics
Logic Minimization
  Karnaugh Maps
Combinational Building Blocks
  Multiplexers
  Decoders
  Encoders
Delays and Timing

## Slide 3: Karnaugh Maps (K-maps)
Graphical method for simplifying Boolean equations
  work well for up to 4 variables
  help quickly combine terms based on visual inspection
Example:
Figure 2.43 Three-input function: (a) truth table, (b) K-map, (c) K-map showing minterms

## Slide 4: Karnaugh Maps
K-Map structure:
  up to 4 variables
    one or two variables  horizontal dimension
    one or two variables  vertical dimension
  rows/columns arranged so only one variable different among neighbors
    ends “wrap around”
Example:

## Slide 5: Logic Minimization using K-Maps
Basic Idea:
  Simply “circle” all “rectangular” regions of 1’s in the K-map
    using the fewest possible number of circles
    each circle should be as large as possible
  Read off the products that were circled
Here are the rules:
  use the fewest circles necessary to cover all the 1’s
  a circle must not contain any 0’s (don’t-cares are okay)
  each circle must span a rectangular block that is a power of 2
    i.e., 1, 2, or 4 squares in each direction
  each circle should be as large as possible
  a circle may wrap around the edges of the K-map
  a 1 in a K-map may be circled multiple times if needed

## Slide 6: An aside on notation
In Boolean equations, complementation can be indicated in one of two ways:
  by using an overbar: e.g.
    best for handwriting or math/equation editors
  by using the prime symbol: e.g., X’
    more convenient for basic wordprocessors

## Slide 7: K-Map: Example 1
The two 1’s can be covered by a single oval
  the circle spans the region expressed as A’B’
  hence, the minimized sum-of-products expression is:

## Slide 8: K-Map: Example 2
Need only two products!
  the four 1’s on the corners can be covered by a single circle
    the 1st circle spans the region B’
  the remaining 1 merges with its neighbor to the right
    the 2nd circle spans AC’
  the minimal SOP expression is:
  the unminimized sum-of-minterms would have been:

## Slide 9: K-Map: Example 3 (with Don’t Cares)
Don’t-Cares can help simplify logic
  a circle may be expanded to include Don’t-Cares
    helps reduce size of product terms
    may help reduce the number of circles
  but Don’t-Cares do not have to be covered
Example:
  if X’s in this K-map were 0’s
    4 products would be needed
    products would be larger

## Slide 10: Combinational Building Blocks
Multiplexers
Decoders
Encoders

## Slide 11: Multiplexer (Mux)
Selects 1 out of N inputs
  a control input (“select” signal) determines which input is chosen
  # bits in select = ceil(log2N)
Example: 2:1 Mux
  2 inputs
  1 output
  1-bit select signal

## Slide 12: Multiplexer Implementations
Logic gates
  Sum-of-products form
Tristate buffers
  For an N-input mux, use N tristate buffers
  Turn on exactly one buffer to propagate the appropriate input
    all others are in floating (Hi-Z) state

## Slide 13: Wider Multiplexers (4:1)
A 4-to-1 mux has 4 inputs and 1 output
  selection signal now is 2 bits
Several ways to implement:
Figure 2.58 4:1 multiplexer implementations: (a) two-level logic, (b) tristates, (c) hierarchical

## Slide 14: Combinational Logic using Multiplexers
Implement a truth table using a mux
  use a mux with as many input lines are rows in the table
  Y values are fed into the mux’s data inputs
  AB values become the mux’s select inputs

## Slide 15: SystemVerilog for Multiplexer
Just a conditional statement:
  module mux(input wire d0, d1,
  input wire s,
  output wire y);
  assign y = s ? d1 : d0;
  endmodule
Easily extends to multi-bit data inputs:
  module mux4bit(input wire [3:0] d0, d1,
  input wire s,
  output wire [3:0] y);
  assign y = s ? d1 : d0;
  endmodule

## Slide 16: SystemVerilog for Multiplexer
Also extends to N-way multiplexers:
  module mux4way4bit(
  input wire [3:0] d0, d1, d2, d3,
  input wire [1:0] s,
  output wire [3:0] y);
  assign y = s[1] ? (s[0]? d3 : d2) : (s[0]? d1 : d0);
  endmodule
Or, in a truth-table style:
  module mux4way4bit(
  input wire [3:0] d0, d1, d2, d3,
  input wire [1:0] s,
  output wire [3:0] y);
  assign y = s == 2’b11 ? d3 :
  s == 2’b10 ? d2 :
  s == 2’b01 ? d1 : d0;
  endmodule

## Slide 17: Decoders
N inputs, 2N outputs
“One-hot” outputs
  only one output HIGH at any given time

## Slide 18: Decoder Implementation
Each output is a minterm!
  Yk = 1 if the inputs A1A0 match corresponding row

## Slide 19: Logic using Decoders
Can implement Boolean function using decoders:
  decoder output is all minterms
  OR the ON-set minterms
Example:
For multiple outputs
  only one decoder needed
  one separate OR gate per output

## Slide 20: Aside: Enable
Enable is a common input to logic functions
  Typically used in memories and some of today’s logic blocks
Two styles:
  EN is ANDed with function
    turns output to 0 when not enabled
  EN’ is ORed with function
    turns output to 1 when not enabled

## Slide 21: Other decoder examples

## Slide 22: Decoder with Enable
When not enabled, all outputs are 0
  otherwise, 2-to-4 decoder

## Slide 23: Decoders
How about a…
  1-to-2 decoder?
  3-to-8 decoder?
  (N)-to-2(N) decoder?
  (N+1)-to-2(N+1) decoder?

## Slide 24: 3-to-8 Decoder: Truth Table
Notice they are minterms

## Slide 25: 3-to-8 Decoder: Schematic

## Slide 26: 3-to-8 Decoder: “Enable” used for expansion

## Slide 27: 3-to-8 Decoder: Multilevel Circuit

## Slide 28: Multi-Level 6-to-64 Decoder
In general: Combine m-to-2m and n-to-2n decoders
  becomes an (m+n)-to-2(m+n) decoder

## Slide 29: Uses for Decoders
Binary number might serve to select some operation
  Number might encode a CPU Instruction (op codes)
    Decoder lines might select add, or subtract, or multiply, etc.
  Number might encode a Memory Address
    To read or write a particular location in memory

## Slide 30: Demultiplexer (demux)
Dual of multiplexer, but a relative of decoder
  One input, multiple outputs (destinations)
  Select signal routes input to one of the outputs
n-bit select implies 2n outputs
  e.g., 4-way demux uses a 2-bit select
  routes input E to one of 4 outputs

## Slide 31: Demux vs. Decoder
Similarities
  decoder produces a “1” on one of the 2N outputs
    … “0” elsewhere
  demultiplexer transmits data to one of the 2N outputs
    … “0” elsewhere
Possible to make one from the other
  How?

## Slide 32: Encoder
Encoder is the opposite of decoder
  2N inputs (or fewer)
  N outputs

## Slide 33: Encoder: Implementation
Inputs are already minterms!
  Simply OR them together appropriately
  e.g.: A0 = D1 + D3 + D5 + D7

## Slide 34: Encoder Implementation: Problem
Specification assumes:
  Only one of the D inputs can be high
What if, say, D3 and D6 are both high?
  simple OR circuit will set A to 7
  so, must modify the spec to avoid this behavior

## Slide 35: Solution: Priority Encoder
Chooses one with highest priority
  Largest number, usually
Note “don’t cares”

## Slide 36: Priority Encoder
What if all inputs are zero?
  Need another output: “Valid”

## Slide 37: Priority Encoder Implementation
Valid is simply the OR of all the data inputs

## Slide 38: Code Converters
General Converters
  convert one code to another
  examples?

## Slide 39: Example: Seven-Segment Display
7-segment display
  convert single hex digit …
  … to a display character code)
Used in the first lab using the hardware kit

## Slide 40: Delays and Timing

## Slide 41: Timing
What is Delay?
  Time from input change to output change
    Transient response
  e.g., rising edge to rising edge
  Usually measured from 50% point

## Slide 42: Types of Delays
Transport delay = “pure” delay
  Whatever goes in …
  … comes out after a specified amount of time
Inertial delay
  Inputs have an effect only if they persist for a specified amount of time
    No effect if input changes and changes back in too short a time (can’t overcome inertia)
    can filter out glitches

## Slide 43: Effect of Transport Delay (blue)
Delay just shifts signal in time
  focus on the blue bars; ignore the black ones
AB

## Slide 44: Effect of Inertial Delay
Changes too close to each other cancel out
  focus on the black bars
AB
Blue – Propagation delay time Black – Rejection time (filter out)

## Slide 45: Propagation & Contamination Delay
Propagation delay: tpd
  max delay from input to output
Contamination delay: tcd
  min delay from input to output

## Slide 46: Propagation & Contamination Delay
Delay is caused by
  Capacitance and resistance in a circuit
    More gates driven, longer delay
    Longer wires at output, longer delay
  Speed of light is the ultimate limitation
Reasons why tpd and tcd may be vary:
  Different rising and falling delays
    What is typically reported? Greater of the two
  Multiple inputs and outputs, some faster than others
  Circuits slow down when hot and speed up when cold
    So, both maximum and typical given
Specs provided in data sheets

## Slide 47: Propagation Delay: Example

## Slide 48: Critical and Short Paths
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR
Short Path: tcd = tcd_AND

## Slide 49: Glitches
What is a Glitch?
  a non-monotonic change in a signal
  e.g., a single input change can cause multiple changes on the same output
  a multi-input transition can also cause glitches
Are glitches a problem?
  Not really in synchronous design
    Clock time period must be long enough for all glitches to subside
  Yes, in asynchronous design
    Absence of clock means there should ideally be no spurious signal transitions, esp. in control signals
  It is important to recognize a glitch when you see one in simulations or on an oscilloscope
  Often cannot get rid of all glitches

## Slide 50: Glitch Example: Self-Study
What happens when:
  A = 0, C = 1, and
  B goes from 1 to 0?
Logically, nothing
  Because although 2nd term goes to false
  1st term now is true
But, output may glitch
  if one input to OR goes low before the other input goes high

## Slide 51: Glitch Example: Self-Study (cont.)

## Slide 52: Glitch Example: Self-Study (cont.)
Fixing the glitch: Add redundant logic term
  A’C
    “bridges the two islands”

## Slide 53: Next
Sequential Design