## Slide 1: Interrupts and System Calls
Don Porter

## Slide 2: First lecture…
App
Hardware
Libraries
Kernel
User
Super- visor
App
Libraries
App
Libraries
System Call Table (350—1200)
Open file “hw1.txt”
Ok, here’s handle 4
Notes: So the OS components in user mode are often called libraries, and the part that runs in super-visor mode is called the kernel.
The kernel itself is often conflated with the OS

## Slide 3: Today’s goal: Key OS building block
Understand how system calls work
  As well as how exceptions (e.g., divide by zero) work
Understand the hardware tools available for irregular control flow.
  I.e., things other than a branch in a running program
Building blocks for context switching, device management, etc.

## Slide 4: Background: Control Flow
// x = 2, y = true
if (y) {
2 /= x;
printf(x);
} //...
void printf(va_args) {
//...
}
Regular control flow: branches and calls (logically follows source code)
pc

## Slide 5: Background: Control Flow
// x = 0, y = true
if (y) {
2 /= x;
printf(x);
} //...
void handle_divzero(){
x = 2;
}
Irregular control flow: exceptions, system calls, etc.
pc
Divide by zero!
Program can’t make progress!

## Slide 6: Two types of interrupts
Synchronous: will happen every time an instruction executes (with a given program state)
  Divide by zero
  System call
  Bad pointer dereference
Asynchronous: caused by an external event
  Usually device I/O
  Timer ticks (well, clocks can be considered a device)

## Slide 7: Asynchronous Interrupt Example
User
Kernel
Stack
Stack
if (x) {
printf(“Boo”);
...
printf(va_args…){
...
Disk_handler (){
...
}
RSP
RIP
RSP
RIP
Disk
Interrupt!

## Slide 8: Intel nomenclature
Interrupt – only refers to asynchronous interrupts
Exception – synchronous control transfer
Note: from the programmer’s perspective, these are handled with the same abstractions

## Slide 9: Lecture outline
Overview
How interrupts work in hardware
How interrupt handlers work in software
How system calls work
Notes: START HERE 2020

## Slide 10: Interrupt overview
Each interrupt or exception includes a number indicating its type
E.g., 14 is a page fault, 3 is a debug breakpoint
This number is the index into an interrupt table

## Slide 11: x86 interrupt table
0
255
…
31
…
…
47
Reserved for
the CPU
Software Configurable
Device IRQs
0x2e = Windows System Call
128 = Linux System Call

## Slide 12: x86 interrupt overview
Each type of interrupt is assigned an index from 0—255.
0—31 are for processor interrupts; generally fixed by Intel
  E.g., 14 is always for page faults
32—255 are software configured
  32—47 are for device interrupts (IRQs)
    Most device’s IRQ line can be configured
    Look up APICs for more info (Ch 4 of Bovet and Cesati)
  0x80 issues system call in Linux (more on this later)

## Slide 13: What happens (high level):
Control jumps to the kernel
  At a prescribed address (the interrupt handler)
The register state of the program is dumped on the kernel’s stack
  Sometimes, extra info is loaded into CPU registers
  E.g., page faults store the address that caused the fault in the cr2 register
Kernel code runs and handles the interrupt
When handler completes, resume program (see iret instr.)

## Slide 14: Important digression: Register state
Really, really, really big idea:
  The state of a program’s execution is succinctly and completely represented by CPU register state
Pause a program: dump the registers in memory
Resume a program: slurp the registers back into CPU
  Be sure to appreciate the power of this idea

## Slide 15: How is this configured?
Kernel creates an array of Interrupt descriptors in memory, called Interrupt Descriptor Table, or IDT
  Can be anywhere in memory
  Pointed to by special register (idtr)
    c.f., segment registers and gdtr and ldtr
Entry 0 configures interrupt 0, and so on

## Slide 16: x86 interrupt table
0
255
…
31
…
…
47
idtr
Linear Address of Interrupt Table

## Slide 17: x86 interrupt table
0
255
…
31
…
…
47
idtr
Code Segment: Kernel Code
Segment Offset: &page_fault_handler //linear addr
Ring: 0 // kernel
Present: 1
Gate Type: Exception
14

## Slide 18: Software interrupts
The int <num> instruction allows software to raise an interrupt
  0x80 is just a Linux convention.
There are a lot of spare indices
  You could have multiple system call tables for different purposes or types of processes!
    Windows does: one for the kernel and one for win32k

## Slide 19: Software interrupts, cont
OS sets ring level required to raise an interrupt
  Generally, user programs can’t issue an int 14 (page fault) manually
  An unauthorized int instruction causes a general protection fault
    Interrupt 13

## Slide 20: Summary
Most interrupt handling hardware state set during boot
Each interrupt has an IDT entry specifying:
  What code to execute, privilege level to raise the interrupt

## Slide 21: Lecture outline
Overview
How interrupts work in hardware
How interrupt handlers work in software
How system calls work

## Slide 22: High-level goal
Respond to some event, return control to the appropriate process
What to do on:
  Network packet arrives
  Disk read completion
  Divide by zero
  System call

## Slide 23: Interrupt Handlers
Just plain old kernel code
  Sort of like exception handlers in Java
  But separated from the control flow of the program
The IDT stores a pointer to the right handler routine

## Slide 24: Lecture outline
Overview
How interrupts work in hardware
How interrupt handlers work in software
How system calls work

## Slide 25: What is a system call?
A function provided to applications by the OS kernel
  Generally to use a hardware abstraction (file, socket)
  Or OS-provided software abstraction (IPC, scheduling)
Why not put these directly in the application?
  Protection of the OS/hardware from buggy/malicious programs
  Applications are not allowed to directly interact with hardware, or access kernel data structures

## Slide 26: System call “interrupt”
Originally, system calls issued using int instruction
Dispatch routine was just an interrupt handler
Like interrupts, system calls are arranged in a table
  See arch/x86/kernel/syscall_table*.S in Linux source
Program selects the system call it wants by placing index in eax register
  Arguments go in the other registers by calling convention
  Return value goes in eax

## Slide 27: Two levels of function pointer tables
0
255
…
31
…
…
47
idtr
128
(system call)
Interrupt Table (CPU automatically walks)
syscall_handler: // Walks syscall table in software
0
~350
…
&sys_read
Syscall Table
&sys_write
&sys_open
&sys_close

## Slide 28: How many system calls?
Linux exports about 350 system calls
Windows exports about 400 system calls for core APIs, and another 800 for GUI methods

## Slide 29: But why use interrupts?
Also protection
Forces applications to call well-defined “public” functions
  Rather than calling arbitrary internal kernel functions
Example (where foo is a system call):
public foo() {
if (!permission_ok()) return –EPERM;
return _foo(); // no permission check
}
Calling _foo() directly would circumvent permission check

## Slide 30: Summary
System calls are the “public” OS APIs
Kernel leverages interrupts to restrict applications to specific functions