## Slide 1: Neuro.ZERO: A Zero-Energy Neural Network Accelerator for Embedded Sensing and Inference Systems
Seulki Lee and Shahriar Nirjon
UNC Chapel Hill
(University of North Carolina at Chapel Hill)
SenSys 2019, November 10-13, 2019, New York, NY, USA

## Slide 2: Battery-Free Smart Devices are the Future
Harvesting energy from sunlight, kinetic, human body…
Advantages: Perpetual, maintenance-free, environment-friendly.
System
Energy
Source

## Slide 3: Problem 1: Intermittent Execution
Energy is not harvestable all the time making systems intermittent.
Device On
Device Off

## Slide 4: Problem 1: Intermittent Execution
Energy is not harvestable all the time making systems intermittent.
Device On
Device Off

## Slide 5: Problem 2: Limited Computation for DNNs
Deep Neural Networks (DNNs) are computationally challenging to embedded devices.
Deep Neural Network (DNN)
MCU
800,000 neurons
100,000 neurons
Compute-intensive
Limited computation-power

## Slide 6: Challenges/Goal
We create a long-term sensing and inference system that provides guaranteed execution of state-of-the-art DNNs.
Guaranteed Execution
DNN Performance Up
Intermittent Execution
Limited Computation for DNNs

## Slide 7: We Propose – Neuro.ZERO
A co-processor architecture consisting of a main MCU that executes scaled-down versions of a DNN with a battery, and an accelerator MCU that is powered by harvested energy.
Intermittent Energy-Aware
Algorithms
Multiple Modes of DNN Execution
Co-MCU
Architecture
+

## Slide 8: We Propose – Neuro.ZERO
A co-processor architecture consisting of a main MCU that executes scaled-down versions of a DNN with a battery, and an accelerator MCU that is powered by harvested energy.
Intermittent Energy-Aware
Algorithms
Multiple Modes of DNN Execution
Co-MCU
Architecture
+

## Slide 9: Neuro.ZERO Architecture
A co-processor architecture: Main MCU + Accelerator MCU
Main MCU
Guaranteed execution
Always on
Accelerator MCU
Opportunistic
performance
improvement
On/Off
Energy-harvester
+
Battery

## Slide 10: Neuro.ZERO Architecture
A co-processor architecture: Main MCU + Accelerator MCU
+
+
Prediction accuracy: 95%
Prediction accuracy: 80%
Guaranteed Execution
Performance up

## Slide 11: Neuro.ZERO vs. Alternatives
Guaranteed Execution
Computation
Scaling
Energy
Efficiency
+
+
Single MCU
Multiple MCU
Neuro.ZERO
Battery-powered MCU
Energy-harvested MCU

## Slide 12: We Propose – Neuro.ZERO
A co-processor architecture consisting of a main MCU that executes scaled-down versions of a DNN with a battery, and an accelerator MCU that is powered by harvested energy.
Intermittent Energy-Aware
Algorithms
Multiple Modes of DNN Execution
Co-MCU
Architecture
+

## Slide 13: Multiple Modes of DNN Execution
Neuro.ZERO supports four acceleration execution of a DNN.
Deep neural network
(DNN)
Mode 1
Inference
Speedup
Mode 3
Multi-DNNs
(Ensemble)
Mode 4
Adaptation
(On-device Training)
Mode 2
Inference
Improvement
Accelerated
Execution of DNN

## Slide 14: Example Application
A traffic sign recognizer DNN for autonomous robots.
A STOP sign ahead.
Delivery robot

## Slide 15: Acceleration Scenario 1: Inference Speedup
Slow running
20 km/h
Fast running
40 km/h
2 seconds
1 second
OK, I’ll use the accelerator as well for faster recognition.
OK, Main MCU is enough.

## Slide 16: Acceleration Scenario 1: Inference Speedup
Inference speedup by offloading a part of the DNN to the accelerator MCU.
Original DNN
(Execution time: 100ms)
Execution time: 100ms
Main MCU
Accelerator MCU
Offloading
+
Execution time: 60ms

## Slide 17: Acceleration Scenario 2: Improved Inference
Busy road! I’ll use the accelerator for
better recognition.
OK, Main MCU is enough.
Crowded road
Open road

## Slide 18: Acceleration Scenario 2: Improved Inference
Performance improvement by extending the DNN (i.e. increasing inference accuracy).
Original DNN
(Accuracy: 80%)
Accuracy: 80%
Accuracy: 95%
Main MCU
Accelerator MCU
+
Extending

## Slide 19: Acceleration Scenario 3: Multi-DNN (Ensemble)
OK, Main MCU is enough.
Snowy
Sunny
Snowy. I cannot see the signs. Let’s use the second camera.
Let’s use the accelerator to run a DNN for the second camera.

## Slide 20: Acceleration Scenario 3: Multi-DNN (Ensemble)
Run a different DNN that provides a second opinion for the task.
Original DNN
(Single DNN)
Original DNN
Ensembled DNN
(Multi-Model DNNs)
Second DNN
Executing
a different DNN
Main MCU
Accelerator MCU
+

## Slide 21: Acceleration Scenario 4: DNN Adaptation
OK, Main MCU is enough.
New road signs
Familiar road signs
What does the sign mean?
OK, Let’s use the accelerator to learn new traffic signs here.

## Slide 22: Acceleration Scenario 4: DNN Adaptation
Enables retraining of the DNN on the accelerator. Training happens separately on the accelerator.
Execute inference
Perform training
DNN model
update
Main MCU
Accelerator MCU
+

## Slide 23: We Propose – Neuro.ZERO
A co-processor architecture consisting of a main MCU that executes scaled-down versions of a DNN with a battery, and an accelerator MCU that is powered by harvested energy.
Intermittent Energy-Aware
Algorithms
Multiple Modes of DNN Execution
Co-MCU
Architecture
+

## Slide 24: Acceleration Algorithm 1: Step-Up Inference
Energy-aware inference acceleration: The amount of acceleration is proportional to the currently-available harvested energy.
Original DNN
(Accuracy: 80%)
Main MCU
+
Extended DNN
(Accuracy: 85%)
Extending
the DNN
Accelerator MCU
Low level of
Harvested energy
Mid level of
Harvested energy
Extended DNN
(Accuracy: 90%)
High level of
Harvested energy
Extended DNN
(Accuracy: 95%)

## Slide 25: Acceleration Algorithm 2: Skip-Out Training
Energy-aware training: Only train a part of the weight parameters proportional to the currently-available harvested energy.
Low harvested energy
Weight to be trained
Weight to be skipped
Mid harvested energy
High harvested energy

## Slide 26: Implementation
App1: Traffic sign recognizer
App2: Voice Command Recognizer
Neuro.Zero Prototype Hardware

## Slide 27: Evaluation: Traffic Sign Recognizer
Main MCU: MSP430 powered by a battery
Accelerator MCU: MSP430 powered by a solar panel
Battery
Solar panel
Dataset: GTSB (43 traffic signs)

## Slide 28: Result: Traffic Sign Recognizer
Inference Speedup
Main MCU
(no accelerator)
Clock-cycle
()
Neuro.ZERO
(Main MCU + Accelerator)
(Low harvested energy)
Neuro.ZERO
(Main MCU + Accelerator)
(High harvested energy)
0
1
2
78%
78%
79%

## Slide 29: Result: Traffic Sign Recognizer
Accuracy Improvement
Main MCU
(no accelerator)
Accuracy
(%)
Neuro.ZERO
(Main MCU + Accelerator)
(Low harvested energy)
Neuro.ZERO
(Main MCU + Accelerator)
(Mid harvested energy)
75
80
90
85
Neuro.ZERO
(Main MCU + Accelerator)
(High harvested energy)
79%
83%
87%
89%

## Slide 30: Result: Traffic Sign Recognizer
Multi-DNNs and Ensemble
Main MCU
(First DNN)
Accuracy
(%)
Neuro.ZERO
Accelerator
(Second DNN)
Neuro.ZERO
Ensembled
(First + Second DNN)
75
80
90
85
82%
83%
86%
+

## Slide 31: Result: Traffic Sign Recognizer
DNN Adaptation: On-Device (Accelerator) Training of DNN
Accuracy (%)
40
50
70
60
10
20
30
0
100
Time (hours)
80
60
40
20
0

## Slide 32: Conclusion
We introduce Neuro.ZERO, an intermittently-powered accelerator that draws no system energy and opportunistically accelerates the performance of a DNN with four modes of accelerations.
To enable zero-energy acceleration, energy-aware acceleration algorithms are proposed.
A traffic sign and a voice command recognizer are implemented, and they have been demonstrated that the inference accuracy and speed increase.
Future Work: Multi-core accelerator architecture

## Slide 33
Thank You